Var     Off-    Variable                                                            Typical
No.     set     Name            Type        Description                             Value         Units
--      ---     ----            ----        -----------                             -----         -----

0       0       isc_enable      char        indicates whether idle speed            1             -- (0,1 or 2)
                                            control (isc) is enabled(>0).
					    If =2, isc will remain enabled
					    after reaching a position. A 1
					    or 2 will allow ctl from +/-
					    button at any time.

1       1       no_cool_cof     char        no. of coefficients for                 0             -- (max of 5)
                                            coolant sensor calibration.
2       2       no_mat_cof      char        no. of coefficients for mfld            0             -- (max of 5)
                                            air temp sensor calibration.
3       3       no_map_cof      char        no. of coefficients for mfld            2             -- (max of 5)
                                            pressure sensor calibration.
4       4       no_tps_cof      char        no. of coefficients for throttle        2             -- (max of 5)
                                            position sensor calibration.
5       5       no_bat_cof      char        no. of coefficients for battery         2             -- (max of 5)
                                            voltage sensor calibration.
6       6       no_baro_cof     char        no. of coefficients for                 2             -- (max of 5)
                                            barometer calibration.
7       8       cool_cof[0]     float       1st coefficient for coolant             --            result in
                                            sensor calibration (polynomial)                       deg Faren x 10
8       12      cool_cof[1]     float       2nd coefficient for coolant             --            result in
                                            sensor calibration                                    deg Faren x 10
9       16      cool_cof[2]     float       3rd coefficient for coolant             --            result in
                                            sensor calibration                                    deg Faren x 10
10      20      cool_cof[3]     float       4th coefficient for coolant             --            result in
                                            sensor calibration                                    deg Faren x 10
11      24      cool_cof[4]     float       5th coefficient for coolant             --            result in
                                            sensor calibration                                    deg Faren x 10

12      28      mat_cof[0]      float       1st coefficient for mfld air            --            result in
                                            temp sensor calibration(poly)                         deg Faren x 10
13      32      mat_cof[1]      float       2nd coefficient for mfld air            --            result in
                                            temp sensor calibration                               deg Faren x 10
14      36      mat_cof[2]      float       3rd coefficient for mfld air            --            result in
                                            temp sensor calibration                               deg Faren x 10
15      40      mat_cof[3]      float       4th coefficient for mfld air            --            result in
                                            temp sensor calibration                               deg Faren x 10
16      44      mat_cof[4]      float       5th coefficient for mfld air            --            result in
                                            temp sensor calibration                               deg Faren x 10

17      48      map_cof[0]      float       1st coefficient for mfld air            143.34        result in
                                            press sensor calibration                              KPa x 10
18      52      map_cof[1]      float       2nd coefficient for mfld air            0.9232038     result in
                                            press sensor calibration                              KPa x 10
19      56      map_cof[2]      float       3rd coefficient for mfld air            ---           result in
                                            press sensor calibration                              KPa x 10
20      60      map_cof[3]      float       4th coefficient for mfld air            ---           result in
                                            press sensor calibration                              KPa x 10
21      64      map_cof[4]      float       5th coefficient for mfld air            ---           result in
                                            press sensor calibration                              KPa x 10

22      68      tps_cof[0]      float       1st coefficient for throttle            -174.512      result in % x
                                            position sensor calibration                           10 fully open
23      72      tps_cof[1]      float       2nd coefficient for throttle            1.1481        result in % x
                                            position sensor calibration                           10 fully open
24      76      tps_cof[2]      float       3rd coefficient for throttle            ---           result in % x
                                            position sensor calibration                           10 fully open
25      80      tps_cof[3]      float       4th coefficient for throttle            ---           result in % x
                                            position sensor calibration                           10 fully open
26      84      tps_cof[4]      float       5th coefficient for throttle            ---           result in % x
                                            position sensor calibration                           10 fully open

27      88      bat_cof[0]      float       1st coefficient for battery             110.0         result in
                                            voltage sensor calibration                            volts x 100
28      92      bat_cof[1]      float       2nd coefficient for battery             2.778993      result in
                                            voltage sensor calibration                            volts x 100
29      96      bat_cof[2]      float       3rd coefficient for battery             ---           result in
                                            voltage sensor calibration                            volts x 100
30      100     bat_cof[3]      float       4th coefficient for battery             ---           result in
                                            voltage sensor calibration                            volts x 100
31      104     bat_cof[4]      float       5th coefficient for battery             ---           result in
                                            voltage sensor calibration                            volts x 100

32      108     baro_cof[0]     float       1st coefficient for barometer           143.34        result in
                                            sensor calibration                                    KPa x 10
33      112     baro_cof[1]     float       2nd coefficient for barometer           0.9232038     result in
                                            sensor calibration                                    KPa x 10
34      116     baro_cof[2]     float       3rd coefficient for barometer           ---           result in
                                            sensor calibration                                    KPa x 10
35      120     baro_cof[3]     float       4th coefficient for barometer           ---           result in
                                            sensor calibration                                    KPa x 10
36      124     baro_cof[4]     float       5th coefficient for barometer           ---           result in
                                            sensor calibration                                    KPa x 10

37      128     accg_cof[0]     float       1st coefficient for accelero-           -5424.0       result in
                                            meter calibration                                     +/-g x 1000
38      132     accg_cof[1]     float       2nd coefficient for accelero-           12.427        result in
                                            meter calibration                                     +/-g x 1000
39      136     accg_cof[2]     float       3rd coefficient for accelero-           ---           result in
                                            meter calibration                                     +/-g x 1000
40      140     accg_cof[3]     float       4th coefficient for accelero-           ---           result in
                                            meter calibration                                     +/-g x 1000
41      144     accg_cof[4]     float       5th coefficient for accelero-           ---           result in
                                            meter calibration                                     +/-g x 1000

42      148     cool_lim1       shrt int    lower limit for coolant sensor          -500          deg Faren x 10
43      150     cool_lim11      shrt int    lower limit for coolant sensor          1700          deg Faren x 10
                                            after warmup period
44      152     cool_lim2       shrt int    upper limit for coolant sensor          2050          deg Faren x 10
45      154     cool_def        shrt int    default value for coolant sensor        1900          deg Faren x 10
46      156     mat_lim1        shrt int    lower limit for mat sensor              -500          deg Faren x 10
47      158     mat_lim2        shrt int    upper limit for mat sensor              2000          deg Faren x 10
48      160     mat_def         shrt int    default value for mat sensor            1000          deg Faren x 10
49      162     map_lim1        shrt int    lower limit for map sensor              150           KPa x 10
                                                                                    (25.1"Hg)
50      164     map_lim2        shrt int    upper limit for map sensor              1090          KPa x 10
51      166     map_def         shrt int    default value for map sensor            550           KPa x 10
                                                                                    (13.3"Hg)
52      168     tps_lim1        shrt int    lower limit for tps sensor              -20           % x 10 fully open
53      170     tps_lim2        shrt int    upper limit for tps sensor              1010          % x 10 fully open
54      172     tps_def         shrt int    default value for tps sensor            250           % x 10 fully open
55      174     bat_lim1        shrt int    lower limit for bat sensor              1100          volts x 100
56      176     bat_lim2        shrt int    upper limit for bat sensor              1500          volts x 100
57      178     bat_def         shrt int    default value for bat sensor            1300          volts x 100
58      180     baro_lim1       shrt int    lower limit for barometer               677           KPa x 10
                                                                                    (20.0"Hg)
59      182     baro_lim2       shrt int    upper limit for barometer               1090          KPa x 10
                                                                                    (32.2"Hg)
60      184     baro_def        shrt int    default value for barometer             1000          KPa x 10
                                                                                    (29.5"Hg)
61      186     inj_lim1        shrt int    lowr limit for injector fault           0             volts x 100
                                            (not currently used)
62      188     inj_lim2        shrt int    uppr limit for injector fault           250           volts x 100
                                            (not currently used)
63      190     t_inj_bkpt      shrt int    time for injector to just barely        600           microsec
                                            open (value is for 12 volts)
64      192     t_inj_ramp      shrt int    time (from breakpoint) for inj to       1400          microsec
                                            fully open (value is for 12 volts)
65      194     t_inj_close     shrt int    time for injector to fully close        1000          microsec

66      196     bat_comp1_slpe  shrt int    rate of compensation to t_inj_          95            microsec/ volt
                                            bkpt for varying battery voltage.
                                            (0 compensation @ 12v)
67      198     bat_comp2_slpe  shrt int    same compensation for t_inj_ramp        95            microsec/ volt

68      200     num_teeth       char        count of nominal number of teeth on     48            --
                                            crank position wheel. num_teeth/4 
					    must be integer
69      201     max_add_teeth   char        number of additional teeth on           1             --
                                            crank position wheel
70      202     deg_per_tooth   char        number of degrees per tooth on          75            deg x 10
                                            crank position wheel (=3600/
					    num_teeth)

71      204     no_temp         shrt int    number of coolant temperatures          13            -- (max of 30)
                                            and points in the tables for
                                            starting, warmup enrichment/
                                            spark & fast idle
72      206     warm_tempa[0]   shrt int    1st element of temperature array        -400          deg Faren x 10
                                            for above tables
73      208     wrm_tempa[1]    shrt int    2nd element of temperature array        -200          deg Faren x 10
74      210     wrm_tempa[2]    shrt int    3rd element of temperature array        0             deg Faren x 10
75      212     wrm_tempa[3]    shrt int    4th element of temperature array        200           deg Faren x 10
76      214     wrm_tempa[4]    shrt int    5th element of temperature array        400           deg Faren x 10
77      216     wrm_tempa[5]    shrt int    6th element of temperature array        600           deg Faren x 10
78      218     wrm_tempa[6]    shrt int    7th element of temperature array        800           deg Faren x 10
79      220     wrm_tempa[7]    shrt int    8th element of temperature array        1000          deg Faren x 10
80      222     wrm_tempa[8]    shrt int    9th element of temperature array        1200          deg Faren x 10
81      224     wrm_tempa[9]    shrt int    10th element of temperature array       1400          deg Faren x 10
82      226     wrm_tempa[10]   shrt int    11th element of temperature array       1600          deg Faren x 10
83      228     wrm_tempa[11]   shrt int    12th element of temperature array       1750          deg Faren x 10
84      230     wrm_tempa[12]   shrt int    13th element of temperature array       1880          deg Faren x 10
                                            for above tables. Note:  if using
                                            extended fast idle after reaching
                                            normal operating temperature (see
                                            ptemp_xisc_const), then last temp-
                                            erature entered in this array should
                                            be the lowest would ever expect
                                            after reaching operating temperature.
85      232     wrm_tempa[13]   shrt int    14th element of temperature array       ---           deg Faren x 10
86      234     wrm_tempa[14]   shrt int    15th element of temperature array       ---           deg Faren x 10
87      236     wrm_tempa[15]   shrt int    16th element of temperature array       ---           deg Faren x 10
88      238     wrm_tempa[16]   shrt int    17th element of temperature array       ---           deg Faren x 10
89      240     wrm_tempa[17]   shrt int    18th element of temperature array       ---           deg Faren x 10
90      242     wrm_tempa[18]   shrt int    19th element of temperature array       ---           deg Faren x 10
91      244     wrm_tempa[19]   shrt int    20th element of temperature array       ---           deg Faren x 10
92      246     wrm_tempa[20]   shrt int    21st element of temperature array       ---           deg Faren x 10
93      248     wrm_tempa[21]   shrt int    22nd element of temperature array       ---           deg Faren x 10
94      250     wrm_tempa[22]   shrt int    23rd element of temperature array       ---           deg Faren x 10
95      252     wrm_tempa[23]   shrt int    24th element of temperature array       ---           deg Faren x 10
96      254     wrm_tempa[24]   shrt int    25th element of temperature array       ---           deg Faren x 10
97      256     wrm_tempa[25]   shrt int    26th element of temperature array       ---           deg Faren x 10
98      258     wrm_tempa[26]   shrt int    27th element of temperature array       ---           deg Faren x 10
99      260     wrm_tempa[27]   shrt int    28th element of temperature array       ---           deg Faren x 10
100     262     wrm_tempa[28]   shrt int    29th element of temperature array       ---           deg Faren x 10
101     264     wrm_tempa[29]   shrt int    30th element of temperature array       ---           deg Faren x 10

102     266     warm_enrich_    shrt int    1st element of warmup enrich-           121           gamma x 100
                table[0]                    ment table. A value of 0 will
                                            leave the A/F ratio at 14.7; a
                                            value of 200 (2 gamma) will
                                            make the ratio 14.7/(1 + 200/100).
                                            Each element corresponds to
                                            element of enrich_tempa
103     268     w_e_table[1]    shrt int    2nd element of we table                 110           gamma x 100
104     270     w_e_table[2]    shrt int    3rd element of we table                 98            gamma x 100
105     272     w_e_table[3]    shrt int    4th element of we table                 87            gamma x 100
106     274     w_e_table[4]    shrt int    5th element of we table                 75            gamma x 100
107     276     w_e_table[5]    shrt int    6th element of we table                 64            gamma x 100
108     278     w_e_table[6]    shrt int    7th element of we table                 53            gamma x 100
109     280     w_e_table[7]    shrt int    8th element of we table                 41            gamma x 100
110     282     w_e_table[8]    shrt int    9th element of we table                 30            gamma x 100
111     284     w_e_table[9]    shrt int    10th element of we table                19            gamma x 100
112     286     w_e_table[10]   shrt int    11th element of we table                8             gamma x 100
113     288     w_e_table[11]   shrt int    12th element of we table                0             gamma x 100
114     290     w_e_table[12]   shrt int    13th element of we table                0             gamma x 100
115     292     w_e_table[13]   shrt int    14th element of we table                ---           gamma x 100
116     294     w_e_table[14]   shrt int    15th element of we table                ---           gamma x 100
117     296     w_e_table[15]   shrt int    16th element of we table                ---           gamma x 100
118     298     w_e_table[16]   shrt int    17th element of we table                ---           gamma x 100
119     300     w_e_table[17]   shrt int    18th element of we table                ---           gamma x 100
120     302     w_e_table[18]   shrt int    19th element of we table                ---           gamma x 100
121     304     w_e_table[19]   shrt int    20th element of we table                ---           gamma x 100
122     306     w_e_table[20]   shrt int    21st element of we table                ---           gamma x 100
123     308     w_e_table[21]   shrt int    22nd element of we table                ---           gamma x 100
124     310     w_e_table[22]   shrt int    23rd element of we table                ---           gamma x 100
125     312     w_e_table[23]   shrt int    24th element of we table                ---           gamma x 100
126     314     w_e_table[24]   shrt int    25th element of we table                ---           gamma x 100
127     316     w_e_table[25]   shrt int    26th element of we table                ---           gamma x 100
128     318     w_e_table[26]   shrt int    27th element of we table                ---           gamma x 100
129     320     w_e_table[27]   shrt int    28th element of we table                ---           gamma x 100
130     322     w_e_table[28]   shrt int    29th element of we table                ---           gamma x 100
131     324     w_e_table[29]   shrt int    30th element of we table                ---           gamma x 100

132     326     warm_spark_     shrt int    1st element of warmup spark             150           deg advance
                table[0]                    advance table. This spark                             @ crank x 10
                                            advance is interpolated as
                                            function of coolant temp,
                                            & is only applied during
                                            warmup.It is added to the
                                            normal advance.
133     328     w_s_table[1]    shrt int    2nd element of ws table                 150           crnk deg x10
134     330     w_s_table[2]    shrt int    3rd element of ws table                 150           crnk deg x10
135     332     w_s_table[3]    shrt int    4th element of ws table                 110           crnk deg x10
136     334     w_s_table[4]    shrt int    5th element of ws table                 88            crnk deg x10
137     336     w_s_table[5]    shrt int    6th element of ws table                 66            crnk deg x10
138     338     w_s_table[6]    shrt int    7th element of ws table                 43            crnk deg x10
139     340     w_s_table[7]    shrt int    8th element of ws table                 21            crnk deg x10
140     342     w_s_table[8]    shrt int    9th element of ws table                 0             crnk deg x10
141     344     w_s_table[9]    shrt int    10th element of ws table                0             crnk deg x10
142     346     w_s_table[10]   shrt int    11th element of ws table                0             crnk deg x10
143     348     w_s_table[11]   shrt int    12th element of ws table                0             crnk deg x10
144     350     w_s_table[12]   shrt int    13th element of ws table                0             crnk deg x10
145     352     w_s_table[13]   shrt int    14th element of ws table                ---           crnk deg x10
146     354     w_s_table[14]   shrt int    15th element of ws table                ---           crnk deg x10
147     356     w_s_table[15]   shrt int    16th element of ws table                ---           crnk deg x10
148     358     w_s_table[16]   shrt int    17th element of ws table                ---           crnk deg x10
149     360     w_s_table[17]   shrt int    18th element of ws table                ---           crnk deg x10
150     362     w_s_table[18]   shrt int    19th element of ws table                ---           crnk deg x10
151     364     w_s_table[19]   shrt int    20th element of ws table                ---           crnk deg x10
152     366     w_s_table[20]   shrt int    21st element of ws table                ---           crnk deg x10
153     368     w_s_table[21]   shrt int    22nd element of ws table                ---           crnk deg x10
154     370     w_s_table[22]   shrt int    23rd element of ws table                ---           crnk deg x10
155     372     w_s_table[23]   shrt int    24th element of ws table                ---           crnk deg x10
156     374     w_s_table[24]   shrt int    25th element of ws table                ---           crnk deg x10
157     376     w_s_table[25]   shrt int    26th element of ws table                ---           crnk deg x10
158     378     w_s_table[26]   shrt int    27th element of ws table                ---           crnk deg x10
159     380     w_s_table[27]   shrt int    28th element of ws table                ---           crnk deg x10
160     382     w_s_table[28]   shrt int    29th element of ws table                ---           crnk deg x10
161     384     w_s_table[29]   shrt int    30th element of ws table                ---           crnk deg x10

162     386     ism_pos_        shrt int    1st element of idle speed               10            steps (0 - max_
                 table[0]                   motor position command                                steps).0 is all
                                            table. These control idle                             way open - very
                                            speed as function of cool-                            fast idle.
                                            ant temperature.
163     388     i_p_table[1]    shrt int    2nd element of ip table                 10            steps
164     390     i_p_table[2]    shrt int    3rd element of ip table                 10            steps
165     392     i_p_table[3]    shrt int    4th element of ip table                 10            steps
166     394     i_p_table[4]    shrt int    5th element of ip table                 26            steps
167     396     i_p_table[5]    shrt int    6th element of ip table                 43            steps
168     398     i_p_table[6]    shrt int    7th element of ip table                 60            steps
169     400     i_p_table[7]    shrt int    8th element of ip table                 75            steps
170     402     i_p_table[8]    shrt int    9th element of ip table                 95            steps
171     404     i_p_table[9]    shrt int    10th element of ip table                115           steps
172     406     i_p_table[10]   shrt int    11th element of ip table                140           steps
173     408     i_p_table[11]   shrt int    12th element of ip table                150           steps
174     410     i_p_table[12]   shrt int    13th element of ip table                160           steps
175     412     i_p_table[13]   shrt int    14th element of ip table                ---           steps
176     414     i_p_table[14]   shrt int    15th element of ip table                ---           steps
177     416     i_p_table[15]   shrt int    16th element of ip table                ---           steps
178     418     i_p_table[16]   shrt int    17th element of ip table                ---           steps
179     420     i_p_table[17]   shrt int    18th element of ip table                ---           steps
180     422     i_p_table[18]   shrt int    19th element of ip table                ---           steps
181     424     i_p_table[19]   shrt int    20th element of ip table                ---           steps
182     426     i_p_table[20]   shrt int    21st element of ip table                ---           steps
183     428     i_p_table[21]   shrt int    22nd element of ip table                ---           steps
184     430     i_p_table[22]   shrt int    23rd element of ip table                ---           steps
185     432     i_p_table[23]   shrt int    24th element of ip table                ---           steps
186     434     i_p_table[24]   shrt int    25th element of ip table                ---           steps
187     436     i_p_table[25]   shrt int    26th element of ip table                ---           steps
188     438     i_p_table[26]   shrt int    27th element of ip table                ---           steps
189     440     i_p_table[27]   shrt int    28th element of ip table                ---           steps
190     442     i_p_table[28]   shrt int    29th element of ip table                ---           steps
191     444     i_p_table[29]   shrt int    30th element of ip table                ---           steps

192     446     acc_temp_       shrt int    1st element of acceleration             0             gamma x 100
                table[0]                    enrichment vs coolant tempera-
                                            ture table. The enrichment is
                                            added during warmup to the
                                            normal acceleration enrichment.
193     448     a_t_table[1]    shrt int    2nd element of at table                 0             gamma x 100
194     450     a_t_table[2]    shrt int    3rd element of at table                 0             gamma x 100
195     452     a_t_table[3]    shrt int    4th element of at table                 0             gamma x 100
196     454     a_t_table[4]    shrt int    5th element of at table                 0             gamma x 100
197     456     a_t_table[5]    shrt int    6th element of at table                 0             gamma x 100
198     458     a_t_table[6]    shrt int    7th element of at table                 0             gamma x 100
199     460     a_t_table[7]    shrt int    8th element of at table                 0             gamma x 100
200     462     a_t_table[8]    shrt int    9th element of at table                 0             gamma x 100
201     464     a_t_table[9]    shrt int    10th element of at table                0             gamma x 100
202     466     a_t_table[10]   shrt int    11th element of at table                0             gamma x 100
203     468     a_t_table[11]   shrt int    12th element of at table                0             gamma x 100
204     470     a_t_table[12]   shrt int    13th element of at table                0             gamma x 100
205     472     a_t_table[13]   shrt int    14th element of at table                ---           gamma x 100
206     474     a_t_table[14]   shrt int    15th element of at table                ---           gamma x 100
207     476     a_t_table[15]   shrt int    16th element of at table                ---           gamma x 100
208     478     a_t_table[16]   shrt int    17th element of at table                ---           gamma x 100
209     480     a_t_table[17]   shrt int    18th element of at table                ---           gamma x 100
210     482     a_t_table[18]   shrt int    19th element of at table                ---           gamma x 100
211     484     a_t_table[19]   shrt int    20th element of at table                ---           gamma x 100
212     486     a_t_table[20]   shrt int    21th element of at table                ---           gamma x 100
213     488     a_t_table[21]   shrt int    22th element of at table                ---           gamma x 100
214     490     a_t_table[22]   shrt int    23th element of at table                ---           gamma x 100
215     492     a_t_table[23]   shrt int    24th element of at table                ---           gamma x 100
216     494     a_t_table[24]   shrt int    25th element of at table                ---           gamma x 100
217     496     a_t_table[25]   shrt int    26th element of at table                ---           gamma x 100
218     498     a_t_table[26]   shrt int    27th element of at table                ---           gamma x 100
219     500     a_t_table[27]   shrt int    28th element of at table                ---           gamma x 100
220     502     a_t_table[28]   shrt int    29th element of at table                ---           gamma x 100
221     504     a_t_table[29]   shrt int    30th element of at table                ---           gamma x 100

222     506     t_strt_enrich   int         duration of initial starting            10000         ms x 10
                                            (cranking) enrichment; begins           (1 sec)
                                            at synch
223     510     t_strt_enrich_  int         duration of tail end of initial         5000          ms x 10
                tail                        starting enrichment, which drops        (0.5 sec)
                                            linearly to 0 over this period
224     514     t_aft_strt_     int         max duration of an enrichment           300000        ms x 10
                enrich                      which also begins at synch, but         (30 sec)
                                            lasts longer, the exact duration being
                                            temperature dependent; this value
                                            is the max possible duration,
                                            corresponding to the coldest expected
                                            temperature (enrich_tempa[0])
225     518     t_aft_strt_     int         same duration as above, but for         80000         ms x 10
                enrich_min                  normal operating temperature            (8 sec)
                                            (enrich_tempa[no_temp - 1]);
                                            the actual duration is interpolated
                                            to a value between the two,
                                            depending on the coolant
                                            temperature at synch
226     522     t_aft_strt_     int         duration of tail end of after-          50000         ms x 10
                enrich_tail                 start enrichment, which drops           (5 sec)
                                            linearly to 0 over this period.
227     526     tmax_we         int         maximum duration of all warmup          9000000       ms x 10
                                            enrichments; only needed in case        (900 sec,
                                            coolant sensor broken - to prevent        15 min)
                                            unecessary calculations; relative
                                            to start of synch
228     530     strt_enrich_    shrt int    fixed enrichment added during           20            gamma x 100
                const                       initial starting (cranking); lasts
                                            from synch to t_strt_enrich +
                                            t_strt_enrich_tail
229     532     strt_enrich_    shrt int    used to calculate a temperature         85            gamma x 100
                tempconst                   dependent enrichment during
                                            initial starting; this value is the
                                            enrichment for the coldest expected
                                            coolant temperature (enrich_tempa[0]);
                                            0 enrichment is used at operating temp,
                                            and the actual starting enrichment is
                                            interpolated between these 2 values
                                            according to coolant temp @ synch;
                                            the enrichment lasts the same as the
                                            fixed enrichment above.
230     534     aft_strt_enrich shrt int    fixed enrichment added during           15            gamma x 100
                _const                      initial warmup; lasts from synch
                                            to  a max (min) of t_aft_strt_enrich
                                            (_min) + t_aft_strt_enrich_tail
231     536     aft_strt_enrich shrt int    used to calculate a temperature         40            gamma x 100
                _tempconst                  dependent enrichment during
                                            initial warmup; this value is the
                                            enrichment for the coldest expected
                                            coolant temperature (enrich_tempa[0]);
                                            0 enrichment is used at operating temp,
                                            and the actual starting enrichment is
                                            interpolated between these 2 values
                                            according to coolant temp @ synch;
                                            the enrichment lasts the same as the
                                            fixed enrichment above.

232     538     t_xisc_const    int         max duration of extended fast           1800000       ms x 10
                                            idle (after reaching normal opera-       (3 min)
                                            ting temperature). May be needed
                                            when very cold, due to oil drag
                                            (oil takes longer than coolant to
                                            heat up). This value for coldest
                                            expected temperature (enrich_
                                            tempa[0]), and 0 duration is used
                                            if startup temp = normal operating
                                            temp. The actual duration is in-
                                            terpolated between them.
233     542     ptemp_xisc_     shrt int    min percent of normal operating         70            % (whole no.)
                const                       temperature (or earliest time) at
                                            which fast idle fall off is halted.
                                            It is then resumed once normal
                                            op temp is reached, but the fall
                                            off is now set so as to reach norm
                                            idle after a duration calculated from
                                            t_xisc_const above. This value is
                                            for coldest temp; 100% is used
                                            if startup temp = norm op temp.

234     544     t_burst         int         duration of initial enrichment          2000          ms x 10
                                            burst for acceleration                  (0.2 sec)
235     548     t_burst_tail    int         duration of tail off of above           1000          ms x 10
                                            enrichment burst to 0                   (0.1 sec)
236     552     t_acc_tail      int         duration of tail off of accelera-       5000          ms x 10
                                            tion enrichment after the accele-       (0.5 sec)
                                            ration is over
237     556     tps_acc         shrt int    threshold rate of change of tps         333           % / sec
                                            required to declare acceleration        (100% open/
                                            is in progress. It is 'or'ed with        0.3 sec)
                                            map_acc.
238     558     map_acc         shrt int    threshold rate of change of map         233           KPa / sec
                                            required to declare acceleration
                                            is in progress. It is 'or'ed with
                                            tps_acc. Set to 4000 to get rid
                                            of this threshold.
239     560     acc0            shrt int    fixed acceleration enrichment           10            gamma x 100
240     562     acc_wght1       float       proportionality factor for accele-      .08000        ((gamma x 100)/
                                            ration enrichment as function of        (0.80          (%/ sec)) x
                                            tps_dot; includes weighting of           wt)          weighting
                                            tps_dot relative to map_dot
241     566     acc_wght2       float       proportionality factor for accele-      .02857        ((gamma x 100)/
                                            ration enrichment as function of        (0.20          (KPa/ sec)) x
                                            map_dot; includes weighting of           wt)          weighting
                                            map_dot relative to tps_dot
242     570     acc_pw0         shrt int    extra fuel pulsewidth added for         1000          microsec
                                            acceleration for period t_burst         (1 ms)
                                            after start of acceleartion, then
                                            tailed off to 0 over period t_burst_
                                            tail.
243     572     acc_burst       shrt int    extra enrichment added for              10            gamma x 100
                                            acceleration for period t_burst
                                            after start of acceleartion, then
                                            tailed off to 0 over period t_burst_
                                            tail.

244     574     ism_maxsteps    shrt int    maximum number of steps in              168           steps
                                            idle speed control motor
245     576     time_bet_steps1 shrt int    time to execute initial ism step        40            ms x 10
                                            command                                 (4 ms)
246     578     time_bet_stepsn shrt int    time to execute final ism step          22            ms x 10
                                            command. Must be < ..._steps1.          (2.2 ms)
247     580     step_rate_cnt   char        If current pos is within step_rate      10            (out of 14 max)
                                            _cnt of desired pos, will only use
                                            time_bet_steps1.

248     582     rev_lim         shrt int    rpm at which rev limiter starts to      7200          rpm
                                            cause random cylinders to miss
                                            (fuel and spark)
249     584     del_rpm         shrt int    rpm band above rev_lim in which         300           rpm
                                            the rev limiter causes random misses
                                            at a progressively higher rate, with
                                            all cylinders killed when rpm above
                                            rev_lim + del_rpm

250     586     mass_air_coeff  float       program constant used to calculate      .175748e-5    ---
                                            the lbs of air entering a cylinder      (=(350/1728)
                                            during an intake stroke; it is =        x (1/8) x
                                            (CID / 1728) x (1 / no. cylinders)      (1/980)x 
                                            x (1 / map( at WOT, in KPa x 10) x       (1/14.7) )
                                            (1/14.7)). map = manifold air press.

251     590     veaf_tble[0][0] float       table of volumetric efficiency and      0.487         ---
                                            A/F tuning vs map (1st slot) and
                                            rpm (2nd slot); the actual number
                                            to be used represents:
                                            VE(@ WOT, as fraction, 0 - 1.0) /
                                            (A/F ratio / 14.7), and is for
                                            the map in veaf_maps[0] and rpm
                                            in veaf_rpms[0]
252     594     ve_tble[ 0][ 1] float       VE for maps[ 0], rpms[1]                0.551         ---
253     598     ve_tble[ 0][ 2] float       VE for maps[ 0], rpms[2]                0.662         ---
254     602     ve_tble[ 0][ 3] float       VE for maps[ 0], rpms[3]                0.735         ---
255     606     ve_tble[ 0][ 4] float       VE for maps[ 0], rpms[4]                0.758         ---
256     610     ve_tble[ 0][ 5] float       VE for maps[ 0], rpms[5]                0.724         ---
257     614     ve_tble[ 0][ 6] float       VE for maps[ 0], rpms[6]                0.805         ---
258     618     ve_tble[ 0][ 7] float       VE for maps[ 0], rpms[7]                0.891         ---
259     622     ve_tble[ 0][ 8] float       VE for maps[ 0], rpms[8]                0.922         ---
260     626     ve_tble[ 0][ 9] float       VE for maps[ 0], rpms[9]                0.937         ---
261     630     ve_tble[ 0][10] float       VE for maps[ 0], rpms[10]               0.929         ---
262     634     ve_tble[ 0][11] float       VE for maps[ 0], rpms[11]               0.919         ---
263     638     ve_tble[ 0][12] float       VE for maps[ 0], rpms[12]               0.875         ---
264     642     ve_tble[ 0][13] float       VE for maps[ 0], rpms[13]               0.827         ---
265     646     ve_tble[ 0][14] float       VE for maps[ 0], rpms[14]               ---           ---
266     650     ve_tble[ 0][15] float       VE for maps[ 0], rpms[15]               ---           ---
267     654     ve_tble[ 0][16] float       VE for maps[ 0], rpms[16]               ---           ---
268     658     ve_tble[ 0][17] float       VE for maps[ 0], rpms[17]               ---           ---
269     662     ve_tble[ 0][18] float       VE for maps[ 0], rpms[18]               ---           ---
270     666     ve_tble[ 0][19] float       VE for maps[ 0], rpms[19]               ---           ---

271     670     ve_tble[ 1][ 0] float       VE for maps[ 1], rpms[0]                0.519         ---
272     674     ve_tble[ 1][ 1] float       VE for maps[ 1], rpms[1]                0.588         ---
273     678     ve_tble[ 1][ 2] float       VE for maps[ 1], rpms[2]                0.706         ---
274     682     ve_tble[ 1][ 3] float       VE for maps[ 1], rpms[3]                0.784         ---
275     686     ve_tble[ 1][ 4] float       VE for maps[ 1], rpms[4]                0.809         ---
276     690     ve_tble[ 1][ 5] float       VE for maps[ 1], rpms[5]                0.772         ---
277     694     ve_tble[ 1][ 6] float       VE for maps[ 1], rpms[6]                0.858         ---
278     698     ve_tble[ 1][ 7] float       VE for maps[ 1], rpms[7]                0.951         ---
279     702     ve_tble[ 1][ 8] float       VE for maps[ 1], rpms[8]                0.983         ---
280     706     ve_tble[ 1][ 9] float       VE for maps[ 1], rpms[9]                1.000         ---
281     710     ve_tble[ 1][10] float       VE for maps[ 1], rpms[10]               0.991         ---
282     714     ve_tble[ 1][11] float       VE for maps[ 1], rpms[11]               0.980         ---
283     718     ve_tble[ 1][12] float       VE for maps[ 1], rpms[12]               0.933         ---
284     722     ve_tble[ 1][13] float       VE for maps[ 1], rpms[13]               0.882         ---
285     726     ve_tble[ 1][14] float       VE for maps[ 1], rpms[14]               ---           ---
286     730     ve_tble[ 1][15] float       VE for maps[ 1], rpms[15]               ---           ---
287     734     ve_tble[ 1][16] float       VE for maps[ 1], rpms[16]               ---           ---
288     738     ve_tble[ 1][17] float       VE for maps[ 1], rpms[17]               ---           ---
289     742     ve_tble[ 1][18] float       VE for maps[ 1], rpms[18]               ---           ---
290     746     ve_tble[ 1][19] float       VE for maps[ 1], rpms[19]               ---           ---

291     750     ve_tble[ 2][ 0] float       VE for maps[ 2], rpms[0]                0.557         ---
292     754     ve_tble[ 2][ 1] float       VE for maps[ 2], rpms[1]                0.630         ---
293     758     ve_tble[ 2][ 2] float       VE for maps[ 2], rpms[2]                0.756         ---
294     762     ve_tble[ 2][ 3] float       VE for maps[ 2], rpms[3]                0.840         ---
295     766     ve_tble[ 2][ 4] float       VE for maps[ 2], rpms[4]                0.866         ---
296     770     ve_tble[ 2][ 5] float       VE for maps[ 2], rpms[5]                0.827         ---
297     774     ve_tble[ 2][ 6] float       VE for maps[ 2], rpms[6]                0.920         ---
298     778     ve_tble[ 2][ 7] float       VE for maps[ 2], rpms[7]                1.019         ---
299     782     ve_tble[ 2][ 8] float       VE for maps[ 2], rpms[8]                1.053         ---
300     786     ve_tble[ 2][ 9] float       VE for maps[ 2], rpms[9]                1.071         ---
301     790     ve_tble[ 2][10] float       VE for maps[ 2], rpms[10]               1.062         ---
302     794     ve_tble[ 2][11] float       VE for maps[ 2], rpms[11]               1.050         ---
303     798     ve_tble[ 2][12] float       VE for maps[ 2], rpms[12]               1.000         ---
304     802     ve_tble[ 2][13] float       VE for maps[ 2], rpms[13]               0.945         ---
305     806     ve_tble[ 2][14] float       VE for maps[ 2], rpms[14]               ---           ---
306     810     ve_tble[ 2][15] float       VE for maps[ 2], rpms[15]               ---           ---
307     814     ve_tble[ 2][16] float       VE for maps[ 2], rpms[16]               ---           ---
308     818     ve_tble[ 2][17] float       VE for maps[ 2], rpms[17]               ---           ---
309     822     ve_tble[ 2][18] float       VE for maps[ 2], rpms[18]               ---           ---
310     826     ve_tble[ 2][19] float       VE for maps[ 2], rpms[19]               ---           ---

311     830     ve_tble[ 3][ 0] float       VE for maps[ 3], rpms[0]                0.623         ---
312     834     ve_tble[ 3][ 1] float       VE for maps[ 3], rpms[1]                0.706         ---
313     838     ve_tble[ 3][ 2] float       VE for maps[ 3], rpms[2]                0.847         ---
314     842     ve_tble[ 3][ 3] float       VE for maps[ 3], rpms[3]                0.941         ---
315     846     ve_tble[ 3][ 4] float       VE for maps[ 3], rpms[4]                0.970         ---
316     850     ve_tble[ 3][ 5] float       VE for maps[ 3], rpms[5]                0.927         ---
317     854     ve_tble[ 3][ 6] float       VE for maps[ 3], rpms[6]                1.030         ---
318     858     ve_tble[ 3][ 7] float       VE for maps[ 3], rpms[7]                1.141         ---
319     862     ve_tble[ 3][ 8] float       VE for maps[ 3], rpms[8]                1.180         ---
320     866     ve_tble[ 3][ 9] float       VE for maps[ 3], rpms[9]                1.200         ---
321     870     ve_tble[ 3][10] float       VE for maps[ 3], rpms[10]               1.189         ---
322     874     ve_tble[ 3][11] float       VE for maps[ 3], rpms[11]               1.176         ---
323     878     ve_tble[ 3][12] float       VE for maps[ 3], rpms[12]               1.120         ---
324     882     ve_tble[ 3][13] float       VE for maps[ 3], rpms[13]               1.058         ---
325     886     ve_tble[ 3][14] float       VE for maps[ 3], rpms[14]               ---           ---
326     890     ve_tble[ 3][15] float       VE for maps[ 3], rpms[15]               ---           ---
327     894     ve_tble[ 3][16] float       VE for maps[ 3], rpms[16]               ---           ---
328     898     ve_tble[ 3][17] float       VE for maps[ 3], rpms[17]               ---           ---
329     902     ve_tble[ 3][18] float       VE for maps[ 3], rpms[18]               ---           ---
330     906     ve_tble[ 3][19] float       VE for maps[ 3], rpms[19]               ---           ---

331     910     ve_tble[ 4][ 0] float       VE for maps[ 4], rpms[0]                0.677         ---
332     914     ve_tble[ 4][ 1] float       VE for maps[ 4], rpms[1]                0.767         ---
333     918     ve_tble[ 4][ 2] float       VE for maps[ 4], rpms[2]                0.920         ---
334     922     ve_tble[ 4][ 3] float       VE for maps[ 4], rpms[3]                1.023         ---
335     926     ve_tble[ 4][ 4] float       VE for maps[ 4], rpms[4]                1.055         ---
336     930     ve_tble[ 4][ 5] float       VE for maps[ 4], rpms[5]                1.007         ---
337     934     ve_tble[ 4][ 6] float       VE for maps[ 4], rpms[6]                1.120         ---
338     938     ve_tble[ 4][ 7] float       VE for maps[ 4], rpms[7]                1.240         ---
339     942     ve_tble[ 4][ 8] float       VE for maps[ 4], rpms[8]                1.282         ---
340     946     ve_tble[ 4][ 9] float       VE for maps[ 4], rpms[9]                1.304         ---
341     950     ve_tble[ 4][10] float       VE for maps[ 4], rpms[10]               1.292         ---
342     954     ve_tble[ 4][11] float       VE for maps[ 4], rpms[11]               1.278         ---
343     958     ve_tble[ 4][12] float       VE for maps[ 4], rpms[12]               1.217         ---
344     962     ve_tble[ 4][13] float       VE for maps[ 4], rpms[13]               1.150         ---
345     966     ve_tble[ 4][14] float       VE for maps[ 4], rpms[14]               ---           ---
346     970     ve_tble[ 4][15] float       VE for maps[ 4], rpms[15]               ---           ---
347     974     ve_tble[ 4][16] float       VE for maps[ 4], rpms[16]               ---           ---
348     978     ve_tble[ 4][17] float       VE for maps[ 4], rpms[17]               ---           ---
349     982     ve_tble[ 4][18] float       VE for maps[ 4], rpms[18]               ---           ---
350     986     ve_tble[ 4][19] float       VE for maps[ 4], rpms[19]               ---           ---

351     990     ve_tble[ 5][ 0] float       VE for maps[ 5], rpms[0]                0.708         ---
352     994     ve_tble[ 5][ 1] float       VE for maps[ 5], rpms[1]                0.802         ---
353     998     ve_tble[ 5][ 2] float       VE for maps[ 5], rpms[2]                0.962         ---
354     1002    ve_tble[ 5][ 3] float       VE for maps[ 5], rpms[3]                1.069         ---
355     1006    ve_tble[ 5][ 4] float       VE for maps[ 5], rpms[4]                1.103         ---
356     1010    ve_tble[ 5][ 5] float       VE for maps[ 5], rpms[5]                1.053         ---
357     1014    ve_tble[ 5][ 6] float       VE for maps[ 5], rpms[6]                1.171         ---
358     1018    ve_tble[ 5][ 7] float       VE for maps[ 5], rpms[7]                1.296         ---
359     1022    ve_tble[ 5][ 8] float       VE for maps[ 5], rpms[8]                1.340         ---
360     1026    ve_tble[ 5][ 9] float       VE for maps[ 5], rpms[9]                1.363         ---
361     1030    ve_tble[ 5][10] float       VE for maps[ 5], rpms[10]               1.351         ---
362     1034    ve_tble[ 5][11] float       VE for maps[ 5], rpms[11]               1.336         ---
363     1038    ve_tble[ 5][12] float       VE for maps[ 5], rpms[12]               1.272         ---
364     1042    ve_tble[ 5][13] float       VE for maps[ 5], rpms[13]               1.203         ---
365     1046    ve_tble[ 5][14] float       VE for maps[ 5], rpms[14]               ---           ---
366     1050    ve_tble[ 5][15] float       VE for maps[ 5], rpms[15]               ---           ---
367     1054    ve_tble[ 5][16] float       VE for maps[ 5], rpms[16]               ---           ---
368     1058    ve_tble[ 5][17] float       VE for maps[ 5], rpms[17]               ---           ---
369     1062    ve_tble[ 5][18] float       VE for maps[ 5], rpms[18]               ---           ---
370     1066    ve_tble[ 5][19] float       VE for maps[ 5], rpms[19]               ---           ---

371     1070    ve_tble[ 6][ 0] float       VE for maps[ 6], rpms[0]                0.708         ---
372     1074    ve_tble[ 6][ 1] float       VE for maps[ 6], rpms[1]                0.802         ---
373     1078    ve_tble[ 6][ 2] float       VE for maps[ 6], rpms[2]                0.962         ---
374     1082    ve_tble[ 6][ 3] float       VE for maps[ 6], rpms[3]                1.069         ---
375     1086    ve_tble[ 6][ 4] float       VE for maps[ 6], rpms[4]                1.103         ---
376     1090    ve_tble[ 6][ 5] float       VE for maps[ 6], rpms[5]                1.053         ---
377     1094    ve_tble[ 6][ 6] float       VE for maps[ 6], rpms[6]                1.171         ---
378     1098    ve_tble[ 6][ 7] float       VE for maps[ 6], rpms[7]                1.296         ---
379     1102    ve_tble[ 6][ 8] float       VE for maps[ 6], rpms[8]                1.340         ---
380     1106    ve_tble[ 6][ 9] float       VE for maps[ 6], rpms[9]                1.363         ---
381     1110    ve_tble[ 6][10] float       VE for maps[ 6], rpms[10]               1.351         ---
382     1114    ve_tble[ 6][11] float       VE for maps[ 6], rpms[11]               1.336         ---
383     1118    ve_tble[ 6][12] float       VE for maps[ 6], rpms[12]               1.272         ---
384     1122    ve_tble[ 6][13] float       VE for maps[ 6], rpms[13]               1.203         ---
385     1126    ve_tble[ 6][14] float       VE for maps[ 6], rpms[14]               ---           ---
386     1130    ve_tble[ 6][15] float       VE for maps[ 6], rpms[15]               ---           ---
387     1134    ve_tble[ 6][16] float       VE for maps[ 6], rpms[16]               ---           ---
388     1138    ve_tble[ 6][17] float       VE for maps[ 6], rpms[17]               ---           ---
389     1142    ve_tble[ 6][18] float       VE for maps[ 6], rpms[18]               ---           ---
390     1146    ve_tble[ 6][19] float       VE for maps[ 6], rpms[19]               ---           ---

391     1150    ve_tble[ 7][ 0] float       VE for maps[ 7], rpms[0]                ---           ---
392     1154    ve_tble[ 7][ 1] float       VE for maps[ 7], rpms[1]                ---           ---
393     1158    ve_tble[ 7][ 2] float       VE for maps[ 7], rpms[2]                ---           ---
394     1162    ve_tble[ 7][ 3] float       VE for maps[ 7], rpms[3]                ---           ---
395     1166    ve_tble[ 7][ 4] float       VE for maps[ 7], rpms[4]                ---           ---
396     1170    ve_tble[ 7][ 5] float       VE for maps[ 7], rpms[5]                ---           ---
397     1174    ve_tble[ 7][ 6] float       VE for maps[ 7], rpms[6]                ---           ---
398     1178    ve_tble[ 7][ 7] float       VE for maps[ 7], rpms[7]                ---           ---
399     1182    ve_tble[ 7][ 8] float       VE for maps[ 7], rpms[8]                ---           ---
400     1186    ve_tble[ 7][ 9] float       VE for maps[ 7], rpms[9]                ---           ---
401     1190    ve_tble[ 7][10] float       VE for maps[ 7], rpms[10]               ---           ---
402     1194    ve_tble[ 7][11] float       VE for maps[ 7], rpms[11]               ---           ---
403     1198    ve_tble[ 7][12] float       VE for maps[ 7], rpms[12]               ---           ---
404     1202    ve_tble[ 7][13] float       VE for maps[ 7], rpms[13]               ---           ---
405     1206    ve_tble[ 7][14] float       VE for maps[ 7], rpms[14]               ---           ---
406     1210    ve_tble[ 7][15] float       VE for maps[ 7], rpms[15]               ---           ---
407     1214    ve_tble[ 7][16] float       VE for maps[ 7], rpms[16]               ---           ---
408     1218    ve_tble[ 7][17] float       VE for maps[ 7], rpms[17]               ---           ---
409     1222    ve_tble[ 7][18] float       VE for maps[ 7], rpms[18]               ---           ---
410     1226    ve_tble[ 7][19] float       VE for maps[ 7], rpms[19]               ---           ---

411     1230    ve_tble[ 8][ 0] float       VE for maps[ 8], rpms[0]                ---           ---
412     1234    ve_tble[ 8][ 1] float       VE for maps[ 8], rpms[1]                ---           ---
413     1238    ve_tble[ 8][ 2] float       VE for maps[ 8], rpms[2]                ---           ---
414     1242    ve_tble[ 8][ 3] float       VE for maps[ 8], rpms[3]                ---           ---
415     1246    ve_tble[ 8][ 4] float       VE for maps[ 8], rpms[4]                ---           ---
416     1250    ve_tble[ 8][ 5] float       VE for maps[ 8], rpms[5]                ---           ---
417     1254    ve_tble[ 8][ 6] float       VE for maps[ 8], rpms[6]                ---           ---
418     1258    ve_tble[ 8][ 7] float       VE for maps[ 8], rpms[7]                ---           ---
419     1262    ve_tble[ 8][ 8] float       VE for maps[ 8], rpms[8]                ---           ---
420     1266    ve_tble[ 8][ 9] float       VE for maps[ 8], rpms[9]                ---           ---
421     1270    ve_tble[ 8][10] float       VE for maps[ 8], rpms[10]               ---           ---
422     1274    ve_tble[ 8][11] float       VE for maps[ 8], rpms[11]               ---           ---
423     1278    ve_tble[ 8][12] float       VE for maps[ 8], rpms[12]               ---           ---
424     1282    ve_tble[ 8][13] float       VE for maps[ 8], rpms[13]               ---           ---
425     1286    ve_tble[ 8][14] float       VE for maps[ 8], rpms[14]               ---           ---
426     1290    ve_tble[ 8][15] float       VE for maps[ 8], rpms[15]               ---           ---
427     1294    ve_tble[ 8][16] float       VE for maps[ 8], rpms[16]               ---           ---
428     1298    ve_tble[ 8][17] float       VE for maps[ 8], rpms[17]               ---           ---
429     1302    ve_tble[ 8][18] float       VE for maps[ 8], rpms[18]               ---           ---
430     1306    ve_tble[ 8][19] float       VE for maps[ 8], rpms[19]               ---           ---

431     1310    ve_tble[ 9][ 0] float       VE for maps[ 9], rpms[0]                ---           ---
432     1314    ve_tble[ 9][ 1] float       VE for maps[ 9], rpms[1]                ---           ---
433     1318    ve_tble[ 9][ 2] float       VE for maps[ 9], rpms[2]                ---           ---
434     1322    ve_tble[ 9][ 3] float       VE for maps[ 9], rpms[3]                ---           ---
435     1326    ve_tble[ 9][ 4] float       VE for maps[ 9], rpms[4]                ---           ---
436     1330    ve_tble[ 9][ 5] float       VE for maps[ 9], rpms[5]                ---           ---
437     1334    ve_tble[ 9][ 6] float       VE for maps[ 9], rpms[6]                ---           ---
438     1338    ve_tble[ 9][ 7] float       VE for maps[ 9], rpms[7]                ---           ---
439     1342    ve_tble[ 9][ 8] float       VE for maps[ 9], rpms[8]                ---           ---
440     1346    ve_tble[ 9][ 9] float       VE for maps[ 9], rpms[9]                ---           ---
441     1350    ve_tble[ 9][10] float       VE for maps[ 9], rpms[10]               ---           ---
442     1354    ve_tble[ 9][11] float       VE for maps[ 9], rpms[11]               ---           ---
443     1358    ve_tble[ 9][12] float       VE for maps[ 9], rpms[12]               ---           ---
444     1362    ve_tble[ 9][13] float       VE for maps[ 9], rpms[13]               ---           ---
445     1366    ve_tble[ 9][14] float       VE for maps[ 9], rpms[14]               ---           ---
446     1370    ve_tble[ 9][15] float       VE for maps[ 9], rpms[15]               ---           ---
447     1374    ve_tble[ 9][16] float       VE for maps[ 9], rpms[16]               ---           ---
448     1378    ve_tble[ 9][17] float       VE for maps[ 9], rpms[17]               ---           ---
449     1382    ve_tble[ 9][18] float       VE for maps[ 9], rpms[18]               ---           ---
450     1386    ve_tble[ 9][19] float       VE for maps[ 9], rpms[19]               ---           ---

451     1390    ve_tble[10][ 0] float       VE for maps[10], rpms[0]                ---           ---
452     1394    ve_tble[10][ 1] float       VE for maps[10], rpms[1]                ---           ---
453     1398    ve_tble[10][ 2] float       VE for maps[10], rpms[2]                ---           ---
454     1402    ve_tble[10][ 3] float       VE for maps[10], rpms[3]                ---           ---
455     1406    ve_tble[10][ 4] float       VE for maps[10], rpms[4]                ---           ---
456     1410    ve_tble[10][ 5] float       VE for maps[10], rpms[5]                ---           ---
457     1414    ve_tble[10][ 6] float       VE for maps[10], rpms[6]                ---           ---
458     1418    ve_tble[10][ 7] float       VE for maps[10], rpms[7]                ---           ---
459     1422    ve_tble[10][ 8] float       VE for maps[10], rpms[8]                ---           ---
460     1426    ve_tble[10][ 9] float       VE for maps[10], rpms[9]                ---           ---
461     1430    ve_tble[10][10] float       VE for maps[10], rpms[10]               ---           ---
462     1434    ve_tble[10][11] float       VE for maps[10], rpms[11]               ---           ---
463     1438    ve_tble[10][12] float       VE for maps[10], rpms[12]               ---           ---
464     1442    ve_tble[10][13] float       VE for maps[10], rpms[13]               ---           ---
465     1446    ve_tble[10][14] float       VE for maps[10], rpms[14]               ---           ---
466     1450    ve_tble[10][15] float       VE for maps[10], rpms[15]               ---           ---
467     1454    ve_tble[10][16] float       VE for maps[10], rpms[16]               ---           ---
468     1458    ve_tble[10][17] float       VE for maps[10], rpms[17]               ---           ---
469     1462    ve_tble[10][18] float       VE for maps[10], rpms[18]               ---           ---
470     1466    ve_tble[10][19] float       VE for maps[10], rpms[19]               ---           ---

471     1470    ve_tble[11][ 0] float       VE for maps[11], rpms[0]                ---           ---
472     1474    ve_tble[11][ 1] float       VE for maps[11], rpms[1]                ---           ---
473     1478    ve_tble[11][ 2] float       VE for maps[11], rpms[2]                ---           ---
474     1482    ve_tble[11][ 3] float       VE for maps[11], rpms[3]                ---           ---
475     1486    ve_tble[11][ 4] float       VE for maps[11], rpms[4]                ---           ---
476     1490    ve_tble[11][ 5] float       VE for maps[11], rpms[5]                ---           ---
477     1494    ve_tble[11][ 6] float       VE for maps[11], rpms[6]                ---           ---
478     1498    ve_tble[11][ 7] float       VE for maps[11], rpms[7]                ---           ---
479     1502    ve_tble[11][ 8] float       VE for maps[11], rpms[8]                ---           ---
480     1506    ve_tble[11][ 9] float       VE for maps[11], rpms[9]                ---           ---
481     1510    ve_tble[11][10] float       VE for maps[11], rpms[10]               ---           ---
482     1514    ve_tble[11][11] float       VE for maps[11], rpms[11]               ---           ---
483     1518    ve_tble[11][12] float       VE for maps[11], rpms[12]               ---           ---
484     1522    ve_tble[11][13] float       VE for maps[11], rpms[13]               ---           ---
485     1526    ve_tble[11][14] float       VE for maps[11], rpms[14]               ---           ---
486     1530    ve_tble[11][15] float       VE for maps[11], rpms[15]               ---           ---
487     1534    ve_tble[11][16] float       VE for maps[11], rpms[16]               ---           ---
488     1538    ve_tble[11][17] float       VE for maps[11], rpms[17]               ---           ---
489     1542    ve_tble[11][18] float       VE for maps[11], rpms[18]               ---           ---
490     1546    ve_tble[11][19] float       VE for maps[11], rpms[19]               ---           ---

491     1550    ve_tble[12][ 0] float       VE for maps[12], rpms[0]                ---           ---
492     1554    ve_tble[12][ 1] float       VE for maps[12], rpms[1]                ---           ---
493     1558    ve_tble[12][ 2] float       VE for maps[12], rpms[2]                ---           ---
494     1562    ve_tble[12][ 3] float       VE for maps[12], rpms[3]                ---           ---
495     1566    ve_tble[12][ 4] float       VE for maps[12], rpms[4]                ---           ---
496     1570    ve_tble[12][ 5] float       VE for maps[12], rpms[5]                ---           ---
497     1574    ve_tble[12][ 6] float       VE for maps[12], rpms[6]                ---           ---
498     1578    ve_tble[12][ 7] float       VE for maps[12], rpms[7]                ---           ---
499     1582    ve_tble[12][ 8] float       VE for maps[12], rpms[8]                ---           ---
500     1586    ve_tble[12][ 9] float       VE for maps[12], rpms[9]                ---           ---
501     1590    ve_tble[12][10] float       VE for maps[12], rpms[10]               ---           ---
502     1594    ve_tble[12][11] float       VE for maps[12], rpms[11]               ---           ---
503     1598    ve_tble[12][12] float       VE for maps[12], rpms[12]               ---           ---
504     1602    ve_tble[12][13] float       VE for maps[12], rpms[13]               ---           ---
505     1606    ve_tble[12][14] float       VE for maps[12], rpms[14]               ---           ---
506     1610    ve_tble[12][15] float       VE for maps[12], rpms[15]               ---           ---
507     1614    ve_tble[12][16] float       VE for maps[12], rpms[16]               ---           ---
508     1618    ve_tble[12][17] float       VE for maps[12], rpms[17]               ---           ---
509     1622    ve_tble[12][18] float       VE for maps[12], rpms[18]               ---           ---
510     1626    ve_tble[12][19] float       VE for maps[12], rpms[19]               ---           ---

511     1630    ve_tble[13][ 0] float       VE for maps[13], rpms[0]                ---           ---
512     1634    ve_tble[13][ 1] float       VE for maps[13], rpms[1]                ---           ---
513     1638    ve_tble[13][ 2] float       VE for maps[13], rpms[2]                ---           ---
514     1642    ve_tble[13][ 3] float       VE for maps[13], rpms[3]                ---           ---
515     1646    ve_tble[13][ 4] float       VE for maps[13], rpms[4]                ---           ---
516     1650    ve_tble[13][ 5] float       VE for maps[13], rpms[5]                ---           ---
517     1654    ve_tble[13][ 6] float       VE for maps[13], rpms[6]                ---           ---
518     1658    ve_tble[13][ 7] float       VE for maps[13], rpms[7]                ---           ---
519     1662    ve_tble[13][ 8] float       VE for maps[13], rpms[8]                ---           ---
520     1666    ve_tble[13][ 9] float       VE for maps[13], rpms[9]                ---           ---
521     1670    ve_tble[13][10] float       VE for maps[13], rpms[10]               ---           ---
522     1674    ve_tble[13][11] float       VE for maps[13], rpms[11]               ---           ---
523     1678    ve_tble[13][12] float       VE for maps[13], rpms[12]               ---           ---
524     1682    ve_tble[13][13] float       VE for maps[13], rpms[13]               ---           ---
525     1686    ve_tble[13][14] float       VE for maps[13], rpms[14]               ---           ---
526     1690    ve_tble[13][15] float       VE for maps[13], rpms[15]               ---           ---
527     1694    ve_tble[13][16] float       VE for maps[13], rpms[16]               ---           ---
528     1698    ve_tble[13][17] float       VE for maps[13], rpms[17]               ---           ---
529     1702    ve_tble[13][18] float       VE for maps[13], rpms[18]               ---           ---
530     1706    ve_tble[13][19] float       VE for maps[13], rpms[19]               ---           ---

531     1710    ve_tble[14][ 0] float       VE for maps[14], rpms[0]                ---           ---
532     1714    ve_tble[14][ 1] float       VE for maps[14], rpms[1]                ---           ---
533     1718    ve_tble[14][ 2] float       VE for maps[14], rpms[2]                ---           ---
534     1722    ve_tble[14][ 3] float       VE for maps[14], rpms[3]                ---           ---
535     1726    ve_tble[14][ 4] float       VE for maps[14], rpms[4]                ---           ---
536     1730    ve_tble[14][ 5] float       VE for maps[14], rpms[5]                ---           ---
537     1734    ve_tble[14][ 6] float       VE for maps[14], rpms[6]                ---           ---
538     1738    ve_tble[14][ 7] float       VE for maps[14], rpms[7]                ---           ---
539     1742    ve_tble[14][ 8] float       VE for maps[14], rpms[8]                ---           ---
540     1746    ve_tble[14][ 9] float       VE for maps[14], rpms[9]                ---           ---
541     1750    ve_tble[14][10] float       VE for maps[14], rpms[10]               ---           ---
542     1754    ve_tble[14][11] float       VE for maps[14], rpms[11]               ---           ---
543     1758    ve_tble[14][12] float       VE for maps[14], rpms[12]               ---           ---
544     1762    ve_tble[14][13] float       VE for maps[14], rpms[13]               ---           ---
545     1766    ve_tble[14][14] float       VE for maps[14], rpms[14]               ---           ---
546     1770    ve_tble[14][15] float       VE for maps[14], rpms[15]               ---           ---
547     1774    ve_tble[14][16] float       VE for maps[14], rpms[16]               ---           ---
548     1778    ve_tble[14][17] float       VE for maps[14], rpms[17]               ---           ---
549     1782    ve_tble[14][18] float       VE for maps[14], rpms[18]               ---           ---
550     1786    ve_tble[14][19] float       VE for maps[14], rpms[19]               ---           ---

551     1790    ve_tble[15][ 0] float       VE for maps[15], rpms[0]                ---           ---
552     1794    ve_tble[15][ 1] float       VE for maps[15], rpms[1]                ---           ---
553     1798    ve_tble[15][ 2] float       VE for maps[15], rpms[2]                ---           ---
554     1802    ve_tble[15][ 3] float       VE for maps[15], rpms[3]                ---           ---
555     1806    ve_tble[15][ 4] float       VE for maps[15], rpms[4]                ---           ---
556     1810    ve_tble[15][ 5] float       VE for maps[15], rpms[5]                ---           ---
557     1814    ve_tble[15][ 6] float       VE for maps[15], rpms[6]                ---           ---
558     1818    ve_tble[15][ 7] float       VE for maps[15], rpms[7]                ---           ---
559     1822    ve_tble[15][ 8] float       VE for maps[15], rpms[8]                ---           ---
560     1826    ve_tble[15][ 9] float       VE for maps[15], rpms[9]                ---           ---
561     1830    ve_tble[15][10] float       VE for maps[15], rpms[10]               ---           ---
562     1834    ve_tble[15][11] float       VE for maps[15], rpms[11]               ---           ---
563     1838    ve_tble[15][12] float       VE for maps[15], rpms[12]               ---           ---
564     1842    ve_tble[15][13] float       VE for maps[15], rpms[13]               ---           ---
565     1846    ve_tble[15][14] float       VE for maps[15], rpms[14]               ---           ---
566     1850    ve_tble[15][15] float       VE for maps[15], rpms[15]               ---           ---
567     1854    ve_tble[15][16] float       VE for maps[15], rpms[16]               ---           ---
568     1858    ve_tble[15][17] float       VE for maps[15], rpms[17]               ---           ---
569     1862    ve_tble[15][18] float       VE for maps[15], rpms[18]               ---           ---
570     1866    ve_tble[15][19] float       VE for maps[15], rpms[19]               ---           ---

571     1870    ve_tble[16][ 0] float       VE for maps[16], rpms[0]                ---           ---
572     1874    ve_tble[16][ 1] float       VE for maps[16], rpms[1]                ---           ---
573     1878    ve_tble[16][ 2] float       VE for maps[16], rpms[2]                ---           ---
574     1882    ve_tble[16][ 3] float       VE for maps[16], rpms[3]                ---           ---
575     1886    ve_tble[16][ 4] float       VE for maps[16], rpms[4]                ---           ---
576     1890    ve_tble[16][ 5] float       VE for maps[16], rpms[5]                ---           ---
577     1894    ve_tble[16][ 6] float       VE for maps[16], rpms[6]                ---           ---
578     1898    ve_tble[16][ 7] float       VE for maps[16], rpms[7]                ---           ---
579     1902    ve_tble[16][ 8] float       VE for maps[16], rpms[8]                ---           ---
580     1906    ve_tble[16][ 9] float       VE for maps[16], rpms[9]                ---           ---
581     1910    ve_tble[16][10] float       VE for maps[16], rpms[10]               ---           ---
582     1914    ve_tble[16][11] float       VE for maps[16], rpms[11]               ---           ---
583     1918    ve_tble[16][12] float       VE for maps[16], rpms[12]               ---           ---
584     1922    ve_tble[16][13] float       VE for maps[16], rpms[13]               ---           ---
585     1926    ve_tble[16][14] float       VE for maps[16], rpms[14]               ---           ---
586     1930    ve_tble[16][15] float       VE for maps[16], rpms[15]               ---           ---
587     1934    ve_tble[16][16] float       VE for maps[16], rpms[16]               ---           ---
588     1938    ve_tble[16][17] float       VE for maps[16], rpms[17]               ---           ---
589     1942    ve_tble[16][18] float       VE for maps[16], rpms[18]               ---           ---
590     1946    ve_tble[16][19] float       VE for maps[16], rpms[19]               ---           ---

591     1950    ve_tble[17][ 0] float       VE for maps[17], rpms[0]                ---           ---
592     1954    ve_tble[17][ 1] float       VE for maps[17], rpms[1]                ---           ---
593     1958    ve_tble[17][ 2] float       VE for maps[17], rpms[2]                ---           ---
594     1962    ve_tble[17][ 3] float       VE for maps[17], rpms[3]                ---           ---
595     1966    ve_tble[17][ 4] float       VE for maps[17], rpms[4]                ---           ---
596     1970    ve_tble[17][ 5] float       VE for maps[17], rpms[5]                ---           ---
597     1974    ve_tble[17][ 6] float       VE for maps[17], rpms[6]                ---           ---
598     1978    ve_tble[17][ 7] float       VE for maps[17], rpms[7]                ---           ---
599     1982    ve_tble[17][ 8] float       VE for maps[17], rpms[8]                ---           ---
600     1986    ve_tble[17][ 9] float       VE for maps[17], rpms[9]                ---           ---
601     1990    ve_tble[17][10] float       VE for maps[17], rpms[10]               ---           ---
602     1994    ve_tble[17][11] float       VE for maps[17], rpms[11]               ---           ---
603     1998    ve_tble[17][12] float       VE for maps[17], rpms[12]               ---           ---
604     2002    ve_tble[17][13] float       VE for maps[17], rpms[13]               ---           ---
605     2006    ve_tble[17][14] float       VE for maps[17], rpms[14]               ---           ---
606     2010    ve_tble[17][15] float       VE for maps[17], rpms[15]               ---           ---
607     2014    ve_tble[17][16] float       VE for maps[17], rpms[16]               ---           ---
608     2018    ve_tble[17][17] float       VE for maps[17], rpms[17]               ---           ---
609     2022    ve_tble[17][18] float       VE for maps[17], rpms[18]               ---           ---
610     2026    ve_tble[17][19] float       VE for maps[17], rpms[19]               ---           ---

611     2030    ve_tble[18][ 0] float       VE for maps[18], rpms[0]                ---           ---
612     2034    ve_tble[18][ 1] float       VE for maps[18], rpms[1]                ---           ---
613     2038    ve_tble[18][ 2] float       VE for maps[18], rpms[2]                ---           ---
614     2042    ve_tble[18][ 3] float       VE for maps[18], rpms[3]                ---           ---
615     2046    ve_tble[18][ 4] float       VE for maps[18], rpms[4]                ---           ---
616     2050    ve_tble[18][ 5] float       VE for maps[18], rpms[5]                ---           ---
617     2054    ve_tble[18][ 6] float       VE for maps[18], rpms[6]                ---           ---
618     2058    ve_tble[18][ 7] float       VE for maps[18], rpms[7]                ---           ---
619     2062    ve_tble[18][ 8] float       VE for maps[18], rpms[8]                ---           ---
620     2066    ve_tble[18][ 9] float       VE for maps[18], rpms[9]                ---           ---
621     2070    ve_tble[18][10] float       VE for maps[18], rpms[10]               ---           ---
622     2074    ve_tble[18][11] float       VE for maps[18], rpms[11]               ---           ---
623     2078    ve_tble[18][12] float       VE for maps[18], rpms[12]               ---           ---
624     2082    ve_tble[18][13] float       VE for maps[18], rpms[13]               ---           ---
625     2086    ve_tble[18][14] float       VE for maps[18], rpms[14]               ---           ---
626     2090    ve_tble[18][15] float       VE for maps[18], rpms[15]               ---           ---
627     2094    ve_tble[18][16] float       VE for maps[18], rpms[16]               ---           ---
628     2098    ve_tble[18][17] float       VE for maps[18], rpms[17]               ---           ---
629     2102    ve_tble[18][18] float       VE for maps[18], rpms[18]               ---           ---
630     2106    ve_tble[18][19] float       VE for maps[18], rpms[19]               ---           ---

631     2110    ve_tble[19][ 0] float       VE for maps[19], rpms[0]                ---           ---
632     2114    ve_tble[19][ 1] float       VE for maps[19], rpms[1]                ---           ---
633     2118    ve_tble[19][ 2] float       VE for maps[19], rpms[2]                ---           ---
634     2122    ve_tble[19][ 3] float       VE for maps[19], rpms[3]                ---           ---
635     2126    ve_tble[19][ 4] float       VE for maps[19], rpms[4]                ---           ---
636     2130    ve_tble[19][ 5] float       VE for maps[19], rpms[5]                ---           ---
637     2134    ve_tble[19][ 6] float       VE for maps[19], rpms[6]                ---           ---
638     2138    ve_tble[19][ 7] float       VE for maps[19], rpms[7]                ---           ---
639     2142    ve_tble[19][ 8] float       VE for maps[19], rpms[8]                ---           ---
640     2146    ve_tble[19][ 9] float       VE for maps[19], rpms[9]                ---           ---
641     2150    ve_tble[19][10] float       VE for maps[19], rpms[10]               ---           ---
642     2154    ve_tble[19][11] float       VE for maps[19], rpms[11]               ---           ---
643     2158    ve_tble[19][12] float       VE for maps[19], rpms[12]               ---           ---
644     2162    ve_tble[19][13] float       VE for maps[19], rpms[13]               ---           ---
645     2166    ve_tble[19][14] float       VE for maps[19], rpms[14]               ---           ---
646     2170    ve_tble[19][15] float       VE for maps[19], rpms[15]               ---           ---
647     2174    ve_tble[19][16] float       VE for maps[19], rpms[16]               ---           ---
648     2178    ve_tble[19][17] float       VE for maps[19], rpms[17]               ---           ---
649     2182    ve_tble[19][18] float       VE for maps[19], rpms[18]               ---           ---
650     2186    ve_tble[19][19] float       VE for maps[19], rpms[19]               ---           ---

651     2190    spark_table     float       table of spark advance vs               0             deg adv @ crank
                [0][0]                      map (1st slot) and rpm (2nd slot);
                                            the number to be used is for
                                            the map in spark_maps[0] and
                                            rpm in spark_rpms[0]
652     2194    sp_tble[ 0][ 1] float       spk adv for maps[ 0], rpms[1]           6             deg adv @ crank
653     2198    sp_tble[ 0][ 2] float       spk adv for maps[ 0], rpms[2]           10            deg adv @ crank
654     2202    sp_tble[ 0][ 3] float       spk adv for maps[ 0], rpms[3]           20            deg adv @ crank
655     2206    sp_tble[ 0][ 4] float       spk adv for maps[ 0], rpms[4]           20            deg adv @ crank
656     2210    sp_tble[ 0][ 5] float       spk adv for maps[ 0], rpms[5]           20            deg adv @ crank
657     2214    sp_tble[ 0][ 6] float       spk adv for maps[ 0], rpms[6]           20            deg adv @ crank
658     2218    sp_tble[ 0][ 7] float       spk adv for maps[ 0], rpms[7]           20            deg adv @ crank
659     2222    sp_tble[ 0][ 8] float       spk adv for maps[ 0], rpms[8]           20            deg adv @ crank
660     2226    sp_tble[ 0][ 9] float       spk adv for maps[ 0], rpms[9]           20            deg adv @ crank
661     2230    sp_tble[ 0][10] float       spk adv for maps[ 0], rpms[10]          20            deg adv @ crank
662     2234    sp_tble[ 0][11] float       spk adv for maps[ 0], rpms[11]          20            deg adv @ crank
663     2238    sp_tble[ 0][12] float       spk adv for maps[ 0], rpms[12]          20            deg adv @ crank
664     2242    sp_tble[ 0][13] float       spk adv for maps[ 0], rpms[13]          20            deg adv @ crank
665     2246    sp_tble[ 0][14] float       spk adv for maps[ 0], rpms[14]          ---           deg adv @ crank
666     2250    sp_tble[ 0][15] float       spk adv for maps[ 0], rpms[15]          ---           deg adv @ crank

667     2254    sp_tble[ 1][ 0] float       spk adv for maps[ 1], rpms[0]           6             deg adv @ crank
668     2258    sp_tble[ 1][ 1] float       spk adv for maps[ 1], rpms[1]           10            deg adv @ crank
669     2262    sp_tble[ 1][ 2] float       spk adv for maps[ 1], rpms[2]           20            deg adv @ crank
670     2266    sp_tble[ 1][ 3] float       spk adv for maps[ 1], rpms[3]           30            deg adv @ crank
671     2270    sp_tble[ 1][ 4] float       spk adv for maps[ 1], rpms[4]           36            deg adv @ crank
672     2274    sp_tble[ 1][ 5] float       spk adv for maps[ 1], rpms[5]           41            deg adv @ crank
673     2278    sp_tble[ 1][ 6] float       spk adv for maps[ 1], rpms[6]           42            deg adv @ crank
674     2282    sp_tble[ 1][ 7] float       spk adv for maps[ 1], rpms[7]           43            deg adv @ crank
675     2286    sp_tble[ 1][ 8] float       spk adv for maps[ 1], rpms[8]           44            deg adv @ crank
676     2290    sp_tble[ 1][ 9] float       spk adv for maps[ 1], rpms[9]           45            deg adv @ crank
677     2294    sp_tble[ 1][10] float       spk adv for maps[ 1], rpms[10]          46            deg adv @ crank
678     2298    sp_tble[ 1][11] float       spk adv for maps[ 1], rpms[11]          46            deg adv @ crank
679     2302    sp_tble[ 1][12] float       spk adv for maps[ 1], rpms[12]          41            deg adv @ crank
680     2306    sp_tble[ 1][13] float       spk adv for maps[ 1], rpms[13]          36            deg adv @ crank
681     2310    sp_tble[ 1][14] float       spk adv for maps[ 1], rpms[14]          ---           deg adv @ crank
682     2314    sp_tble[ 1][15] float       spk adv for maps[ 1], rpms[15]          ---           deg adv @ crank

683     2318    sp_tble[ 2][ 0] float       spk adv for maps[ 2], rpms[0]           6             deg adv @ crank
684     2322    sp_tble[ 2][ 1] float       spk adv for maps[ 2], rpms[1]           10            deg adv @ crank
685     2326    sp_tble[ 2][ 2] float       spk adv for maps[ 2], rpms[2]           20            deg adv @ crank
686     2330    sp_tble[ 2][ 3] float       spk adv for maps[ 2], rpms[3]           30            deg adv @ crank
687     2334    sp_tble[ 2][ 4] float       spk adv for maps[ 2], rpms[4]           36            deg adv @ crank
688     2338    sp_tble[ 2][ 5] float       spk adv for maps[ 2], rpms[5]           41            deg adv @ crank
689     2342    sp_tble[ 2][ 6] float       spk adv for maps[ 2], rpms[6]           42            deg adv @ crank
690     2346    sp_tble[ 2][ 7] float       spk adv for maps[ 2], rpms[7]           43            deg adv @ crank
691     2350    sp_tble[ 2][ 8] float       spk adv for maps[ 2], rpms[8]           44            deg adv @ crank
692     2354    sp_tble[ 2][ 9] float       spk adv for maps[ 2], rpms[9]           45            deg adv @ crank
693     2358    sp_tble[ 2][10] float       spk adv for maps[ 2], rpms[10]          46            deg adv @ crank
694     2362    sp_tble[ 2][11] float       spk adv for maps[ 2], rpms[11]          46            deg adv @ crank
695     2366    sp_tble[ 2][12] float       spk adv for maps[ 2], rpms[12]          41            deg adv @ crank
696     2370    sp_tble[ 2][13] float       spk adv for maps[ 2], rpms[13]          36            deg adv @ crank
697     2374    sp_tble[ 2][14] float       spk adv for maps[ 2], rpms[14]          ---           deg adv @ crank
698     2378    sp_tble[ 2][15] float       spk adv for maps[ 2], rpms[15]          ---           deg adv @ crank

699     2382    sp_tble[ 3][ 0] float       spk adv for maps[ 3], rpms[0]           6             deg adv @ crank
700     2386    sp_tble[ 3][ 1] float       spk adv for maps[ 3], rpms[1]           10            deg adv @ crank
701     2390    sp_tble[ 3][ 2] float       spk adv for maps[ 3], rpms[2]           20            deg adv @ crank
702     2394    sp_tble[ 3][ 3] float       spk adv for maps[ 3], rpms[3]           30            deg adv @ crank
703     2398    sp_tble[ 3][ 4] float       spk adv for maps[ 3], rpms[4]           36            deg adv @ crank
704     2402    sp_tble[ 3][ 5] float       spk adv for maps[ 3], rpms[5]           41            deg adv @ crank
705     2406    sp_tble[ 3][ 6] float       spk adv for maps[ 3], rpms[6]           42            deg adv @ crank
706     2410    sp_tble[ 3][ 7] float       spk adv for maps[ 3], rpms[7]           43            deg adv @ crank
707     2414    sp_tble[ 3][ 8] float       spk adv for maps[ 3], rpms[8]           44            deg adv @ crank
708     2418    sp_tble[ 3][ 9] float       spk adv for maps[ 3], rpms[9]           45            deg adv @ crank
709     2422    sp_tble[ 3][10] float       spk adv for maps[ 3], rpms[10]          46            deg adv @ crank
710     2426    sp_tble[ 3][11] float       spk adv for maps[ 3], rpms[11]          46            deg adv @ crank
711     2430    sp_tble[ 3][12] float       spk adv for maps[ 3], rpms[12]          41            deg adv @ crank
712     2434    sp_tble[ 3][13] float       spk adv for maps[ 3], rpms[13]          36            deg adv @ crank
713     2438    sp_tble[ 3][14] float       spk adv for maps[ 3], rpms[14]          ---           deg adv @ crank
714     2442    sp_tble[ 3][15] float       spk adv for maps[ 3], rpms[15]          ---           deg adv @ crank

715     2446    sp_tble[ 4][ 0] float       spk adv for maps[ 4], rpms[0]           6             deg adv @ crank
716     2450    sp_tble[ 4][ 1] float       spk adv for maps[ 4], rpms[1]           10            deg adv @ crank
717     2454    sp_tble[ 4][ 2] float       spk adv for maps[ 4], rpms[2]           18            deg adv @ crank
718     2458    sp_tble[ 4][ 3] float       spk adv for maps[ 4], rpms[3]           26            deg adv @ crank
719     2462    sp_tble[ 4][ 4] float       spk adv for maps[ 4], rpms[4]           32            deg adv @ crank
720     2466    sp_tble[ 4][ 5] float       spk adv for maps[ 4], rpms[5]           37            deg adv @ crank
721     2470    sp_tble[ 4][ 6] float       spk adv for maps[ 4], rpms[6]           38            deg adv @ crank
722     2474    sp_tble[ 4][ 7] float       spk adv for maps[ 4], rpms[7]           39            deg adv @ crank
723     2478    sp_tble[ 4][ 8] float       spk adv for maps[ 4], rpms[8]           40            deg adv @ crank
724     2482    sp_tble[ 4][ 9] float       spk adv for maps[ 4], rpms[9]           41            deg adv @ crank
725     2486    sp_tble[ 4][10] float       spk adv for maps[ 4], rpms[10]          42            deg adv @ crank
726     2490    sp_tble[ 4][11] float       spk adv for maps[ 4], rpms[11]          42            deg adv @ crank
727     2494    sp_tble[ 4][12] float       spk adv for maps[ 4], rpms[12]          39            deg adv @ crank
728     2498    sp_tble[ 4][13] float       spk adv for maps[ 4], rpms[13]          36            deg adv @ crank
729     2502    sp_tble[ 4][14] float       spk adv for maps[ 4], rpms[14]          ---           deg adv @ crank
730     2506    sp_tble[ 4][15] float       spk adv for maps[ 4], rpms[15]          ---           deg adv @ crank

731     2510    sp_tble[ 5][ 0] float       spk adv for maps[ 5], rpms[0]           6             deg adv @ crank
732     2514    sp_tble[ 5][ 1] float       spk adv for maps[ 5], rpms[1]           10            deg adv @ crank
733     2518    sp_tble[ 5][ 2] float       spk adv for maps[ 5], rpms[2]           17            deg adv @ crank
734     2522    sp_tble[ 5][ 3] float       spk adv for maps[ 5], rpms[3]           24            deg adv @ crank
735     2526    sp_tble[ 5][ 4] float       spk adv for maps[ 5], rpms[4]           30            deg adv @ crank
736     2530    sp_tble[ 5][ 5] float       spk adv for maps[ 5], rpms[5]           35            deg adv @ crank
737     2534    sp_tble[ 5][ 6] float       spk adv for maps[ 5], rpms[6]           36            deg adv @ crank
738     2538    sp_tble[ 5][ 7] float       spk adv for maps[ 5], rpms[7]           37            deg adv @ crank
739     2542    sp_tble[ 5][ 8] float       spk adv for maps[ 5], rpms[8]           38            deg adv @ crank
740     2546    sp_tble[ 5][ 9] float       spk adv for maps[ 5], rpms[9]           39            deg adv @ crank
741     2550    sp_tble[ 5][10] float       spk adv for maps[ 5], rpms[10]          40            deg adv @ crank
742     2554    sp_tble[ 5][11] float       spk adv for maps[ 5], rpms[11]          40            deg adv @ crank
743     2558    sp_tble[ 5][12] float       spk adv for maps[ 5], rpms[12]          38            deg adv @ crank
744     2562    sp_tble[ 5][13] float       spk adv for maps[ 5], rpms[13]          36            deg adv @ crank
745     2566    sp_tble[ 5][14] float       spk adv for maps[ 5], rpms[14]          ---           deg adv @ crank
746     2570    sp_tble[ 5][15] float       spk adv for maps[ 5], rpms[15]          ---           deg adv @ crank

747     2574    sp_tble[ 6][ 0] float       spk adv for maps[ 6], rpms[0]           6             deg adv @ crank
748     2578    sp_tble[ 6][ 1] float       spk adv for maps[ 6], rpms[1]           10            deg adv @ crank
749     2582    sp_tble[ 6][ 2] float       spk adv for maps[ 6], rpms[2]           16            deg adv @ crank
750     2586    sp_tble[ 6][ 3] float       spk adv for maps[ 6], rpms[3]           22            deg adv @ crank
751     2590    sp_tble[ 6][ 4] float       spk adv for maps[ 6], rpms[4]           28            deg adv @ crank
752     2594    sp_tble[ 6][ 5] float       spk adv for maps[ 6], rpms[5]           33            deg adv @ crank
753     2598    sp_tble[ 6][ 6] float       spk adv for maps[ 6], rpms[6]           34            deg adv @ crank
754     2602    sp_tble[ 6][ 7] float       spk adv for maps[ 6], rpms[7]           35            deg adv @ crank
755     2606    sp_tble[ 6][ 8] float       spk adv for maps[ 6], rpms[8]           36            deg adv @ crank
756     2610    sp_tble[ 6][ 9] float       spk adv for maps[ 6], rpms[9]           37            deg adv @ crank
757     2614    sp_tble[ 6][10] float       spk adv for maps[ 6], rpms[10]          38            deg adv @ crank
758     2618    sp_tble[ 6][11] float       spk adv for maps[ 6], rpms[11]          38            deg adv @ crank
759     2622    sp_tble[ 6][12] float       spk adv for maps[ 6], rpms[12]          37            deg adv @ crank
760     2626    sp_tble[ 6][13] float       spk adv for maps[ 6], rpms[13]          36            deg adv @ crank
761     2630    sp_tble[ 6][14] float       spk adv for maps[ 6], rpms[14]          ---           deg adv @ crank
762     2634    sp_tble[ 6][15] float       spk adv for maps[ 6], rpms[15]          ---           deg adv @ crank

763     2638    sp_tble[ 7][ 0] float       spk adv for maps[ 7], rpms[0]           6             deg adv @ crank
764     2642    sp_tble[ 7][ 1] float       spk adv for maps[ 7], rpms[1]           10            deg adv @ crank
765     2646    sp_tble[ 7][ 2] float       spk adv for maps[ 7], rpms[2]           15            deg adv @ crank
766     2650    sp_tble[ 7][ 3] float       spk adv for maps[ 7], rpms[3]           20            deg adv @ crank
767     2654    sp_tble[ 7][ 4] float       spk adv for maps[ 7], rpms[4]           26            deg adv @ crank
768     2658    sp_tble[ 7][ 5] float       spk adv for maps[ 7], rpms[5]           31            deg adv @ crank
769     2662    sp_tble[ 7][ 6] float       spk adv for maps[ 7], rpms[6]           32            deg adv @ crank
770     2666    sp_tble[ 7][ 7] float       spk adv for maps[ 7], rpms[7]           33            deg adv @ crank
771     2670    sp_tble[ 7][ 8] float       spk adv for maps[ 7], rpms[8]           34            deg adv @ crank
772     2674    sp_tble[ 7][ 9] float       spk adv for maps[ 7], rpms[9]           35            deg adv @ crank
773     2678    sp_tble[ 7][10] float       spk adv for maps[ 7], rpms[10]          36            deg adv @ crank
774     2682    sp_tble[ 7][11] float       spk adv for maps[ 7], rpms[11]          36            deg adv @ crank
775     2686    sp_tble[ 7][12] float       spk adv for maps[ 7], rpms[12]          36            deg adv @ crank
776     2690    sp_tble[ 7][13] float       spk adv for maps[ 7], rpms[13]          36            deg adv @ crank
777     2694    sp_tble[ 7][14] float       spk adv for maps[ 7], rpms[14]          ---           deg adv @ crank
778     2698    sp_tble[ 7][15] float       spk adv for maps[ 7], rpms[15]          ---           deg adv @ crank

779     2702    sp_tble[ 8][ 0] float       spk adv for maps[ 8], rpms[0]           6             deg adv @ crank
780     2706    sp_tble[ 8][ 1] float       spk adv for maps[ 8], rpms[1]           10            deg adv @ crank
781     2710    sp_tble[ 8][ 2] float       spk adv for maps[ 8], rpms[2]           15            deg adv @ crank
782     2714    sp_tble[ 8][ 3] float       spk adv for maps[ 8], rpms[3]           20            deg adv @ crank
783     2718    sp_tble[ 8][ 4] float       spk adv for maps[ 8], rpms[4]           26            deg adv @ crank
784     2722    sp_tble[ 8][ 5] float       spk adv for maps[ 8], rpms[5]           31            deg adv @ crank
785     2726    sp_tble[ 8][ 6] float       spk adv for maps[ 8], rpms[6]           32            deg adv @ crank
786     2730    sp_tble[ 8][ 7] float       spk adv for maps[ 8], rpms[7]           33            deg adv @ crank
787     2734    sp_tble[ 8][ 8] float       spk adv for maps[ 8], rpms[8]           34            deg adv @ crank
788     2738    sp_tble[ 8][ 9] float       spk adv for maps[ 8], rpms[9]           35            deg adv @ crank
789     2742    sp_tble[ 8][10] float       spk adv for maps[ 8], rpms[10]          36            deg adv @ crank
790     2746    sp_tble[ 8][11] float       spk adv for maps[ 8], rpms[11]          36            deg adv @ crank
791     2750    sp_tble[ 8][12] float       spk adv for maps[ 8], rpms[12]          36            deg adv @ crank
792     2754    sp_tble[ 8][13] float       spk adv for maps[ 8], rpms[13]          36            deg adv @ crank
793     2758    sp_tble[ 8][14] float       spk adv for maps[ 8], rpms[14]          ---           deg adv @ crank
794     2762    sp_tble[ 8][15] float       spk adv for maps[ 8], rpms[15]          ---           deg adv @ crank

795     2766    sp_tble[ 9][ 0] float       spk adv for maps[ 9], rpms[0]           ---           deg adv @ crank
796     2770    sp_tble[ 9][ 1] float       spk adv for maps[ 9], rpms[1]           ---           deg adv @ crank
797     2774    sp_tble[ 9][ 2] float       spk adv for maps[ 9], rpms[2]           ---           deg adv @ crank
798     2778    sp_tble[ 9][ 3] float       spk adv for maps[ 9], rpms[3]           ---           deg adv @ crank
799     2782    sp_tble[ 9][ 4] float       spk adv for maps[ 9], rpms[4]           ---           deg adv @ crank
800     2786    sp_tble[ 9][ 5] float       spk adv for maps[ 9], rpms[5]           ---           deg adv @ crank
801     2790    sp_tble[ 9][ 6] float       spk adv for maps[ 9], rpms[6]           ---           deg adv @ crank
802     2794    sp_tble[ 9][ 7] float       spk adv for maps[ 9], rpms[7]           ---           deg adv @ crank
803     2798    sp_tble[ 9][ 8] float       spk adv for maps[ 9], rpms[8]           ---           deg adv @ crank
804     2802    sp_tble[ 9][ 9] float       spk adv for maps[ 9], rpms[9]           ---           deg adv @ crank
805     2806    sp_tble[ 9][10] float       spk adv for maps[ 9], rpms[10]          ---           deg adv @ crank
806     2810    sp_tble[ 9][11] float       spk adv for maps[ 9], rpms[11]          ---           deg adv @ crank
807     2814    sp_tble[ 9][12] float       spk adv for maps[ 9], rpms[12]          ---           deg adv @ crank
808     2818    sp_tble[ 9][13] float       spk adv for maps[ 9], rpms[13]          ---           deg adv @ crank
809     2822    sp_tble[ 9][14] float       spk adv for maps[ 9], rpms[14]          ---           deg adv @ crank
810     2826    sp_tble[ 9][15] float       spk adv for maps[ 9], rpms[15]          ---           deg adv @ crank

811     2830    sp_tble[10][ 0] float       spk adv for maps[10], rpms[0]           ---           deg adv @ crank
812     2834    sp_tble[10][ 1] float       spk adv for maps[10], rpms[1]           ---           deg adv @ crank
813     2838    sp_tble[10][ 2] float       spk adv for maps[10], rpms[2]           ---           deg adv @ crank
814     2842    sp_tble[10][ 3] float       spk adv for maps[10], rpms[3]           ---           deg adv @ crank
815     2846    sp_tble[10][ 4] float       spk adv for maps[10], rpms[4]           ---           deg adv @ crank
816     2850    sp_tble[10][ 5] float       spk adv for maps[10], rpms[5]           ---           deg adv @ crank
817     2854    sp_tble[10][ 6] float       spk adv for maps[10], rpms[6]           ---           deg adv @ crank
818     2858    sp_tble[10][ 7] float       spk adv for maps[10], rpms[7]           ---           deg adv @ crank
819     2862    sp_tble[10][ 8] float       spk adv for maps[10], rpms[8]           ---           deg adv @ crank
820     2866    sp_tble[10][ 9] float       spk adv for maps[10], rpms[9]           ---           deg adv @ crank
821     2870    sp_tble[10][10] float       spk adv for maps[10], rpms[10]          ---           deg adv @ crank
822     2874    sp_tble[10][11] float       spk adv for maps[10], rpms[11]          ---           deg adv @ crank
823     2878    sp_tble[10][12] float       spk adv for maps[10], rpms[12]          ---           deg adv @ crank
824     2882    sp_tble[10][13] float       spk adv for maps[10], rpms[13]          ---           deg adv @ crank
825     2886    sp_tble[10][14] float       spk adv for maps[10], rpms[14]          ---           deg adv @ crank
826     2890    sp_tble[10][15] float       spk adv for maps[10], rpms[15]          ---           deg adv @ crank

827     2894    sp_tble[11][ 0] float       spk adv for maps[11], rpms[0]           ---           deg adv @ crank
828     2898    sp_tble[11][ 1] float       spk adv for maps[11], rpms[1]           ---           deg adv @ crank
829     2902    sp_tble[11][ 2] float       spk adv for maps[11], rpms[2]           ---           deg adv @ crank
830     2906    sp_tble[11][ 3] float       spk adv for maps[11], rpms[3]           ---           deg adv @ crank
831     2910    sp_tble[11][ 4] float       spk adv for maps[11], rpms[4]           ---           deg adv @ crank
832     2914    sp_tble[11][ 5] float       spk adv for maps[11], rpms[5]           ---           deg adv @ crank
833     2918    sp_tble[11][ 6] float       spk adv for maps[11], rpms[6]           ---           deg adv @ crank
834     2922    sp_tble[11][ 7] float       spk adv for maps[11], rpms[7]           ---           deg adv @ crank
835     2926    sp_tble[11][ 8] float       spk adv for maps[11], rpms[8]           ---           deg adv @ crank
836     2930    sp_tble[11][ 9] float       spk adv for maps[11], rpms[9]           ---           deg adv @ crank
837     2934    sp_tble[11][10] float       spk adv for maps[11], rpms[10]          ---           deg adv @ crank
838     2938    sp_tble[11][11] float       spk adv for maps[11], rpms[11]          ---           deg adv @ crank
839     2942    sp_tble[11][12] float       spk adv for maps[11], rpms[12]          ---           deg adv @ crank
840     2946    sp_tble[11][13] float       spk adv for maps[11], rpms[13]          ---           deg adv @ crank
841     2950    sp_tble[11][14] float       spk adv for maps[11], rpms[14]          ---           deg adv @ crank
842     2954    sp_tble[11][15] float       spk adv for maps[11], rpms[15]          ---           deg adv @ crank

843     2958    sp_tble[12][ 0] float       spk adv for maps[12], rpms[0]           ---           deg adv @ crank
844     2962    sp_tble[12][ 1] float       spk adv for maps[12], rpms[1]           ---           deg adv @ crank
845     2966    sp_tble[12][ 2] float       spk adv for maps[12], rpms[2]           ---           deg adv @ crank
846     2970    sp_tble[12][ 3] float       spk adv for maps[12], rpms[3]           ---           deg adv @ crank
847     2974    sp_tble[12][ 4] float       spk adv for maps[12], rpms[4]           ---           deg adv @ crank
848     2978    sp_tble[12][ 5] float       spk adv for maps[12], rpms[5]           ---           deg adv @ crank
849     2982    sp_tble[12][ 6] float       spk adv for maps[12], rpms[6]           ---           deg adv @ crank
850     2986    sp_tble[12][ 7] float       spk adv for maps[12], rpms[7]           ---           deg adv @ crank
851     2990    sp_tble[12][ 8] float       spk adv for maps[12], rpms[8]           ---           deg adv @ crank
852     2994    sp_tble[12][ 9] float       spk adv for maps[12], rpms[9]           ---           deg adv @ crank
853     2998    sp_tble[12][10] float       spk adv for maps[12], rpms[10]          ---           deg adv @ crank
854     3002    sp_tble[12][11] float       spk adv for maps[12], rpms[11]          ---           deg adv @ crank
855     3006    sp_tble[12][12] float       spk adv for maps[12], rpms[12]          ---           deg adv @ crank
856     3010    sp_tble[12][13] float       spk adv for maps[12], rpms[13]          ---           deg adv @ crank
857     3014    sp_tble[12][14] float       spk adv for maps[12], rpms[14]          ---           deg adv @ crank
858     3018    sp_tble[12][15] float       spk adv for maps[12], rpms[15]          ---           deg adv @ crank

859     3022    sp_tble[13][ 0] float       spk adv for maps[13], rpms[0]           ---           deg adv @ crank
860     3026    sp_tble[13][ 1] float       spk adv for maps[13], rpms[1]           ---           deg adv @ crank
861     3030    sp_tble[13][ 2] float       spk adv for maps[13], rpms[2]           ---           deg adv @ crank
862     3034    sp_tble[13][ 3] float       spk adv for maps[13], rpms[3]           ---           deg adv @ crank
863     3038    sp_tble[13][ 4] float       spk adv for maps[13], rpms[4]           ---           deg adv @ crank
864     3042    sp_tble[13][ 5] float       spk adv for maps[13], rpms[5]           ---           deg adv @ crank
865     3046    sp_tble[13][ 6] float       spk adv for maps[13], rpms[6]           ---           deg adv @ crank
866     3050    sp_tble[13][ 7] float       spk adv for maps[13], rpms[7]           ---           deg adv @ crank
867     3054    sp_tble[13][ 8] float       spk adv for maps[13], rpms[8]           ---           deg adv @ crank
868     3058    sp_tble[13][ 9] float       spk adv for maps[13], rpms[9]           ---           deg adv @ crank
869     3062    sp_tble[13][10] float       spk adv for maps[13], rpms[10]          ---           deg adv @ crank
870     3066    sp_tble[13][11] float       spk adv for maps[13], rpms[11]          ---           deg adv @ crank
871     3070    sp_tble[13][12] float       spk adv for maps[13], rpms[12]          ---           deg adv @ crank
872     3074    sp_tble[13][13] float       spk adv for maps[13], rpms[13]          ---           deg adv @ crank
873     3078    sp_tble[13][14] float       spk adv for maps[13], rpms[14]          ---           deg adv @ crank
874     3082    sp_tble[13][15] float       spk adv for maps[13], rpms[15]          ---           deg adv @ crank

875     3086    sp_tble[14][ 0] float       spk adv for maps[14], rpms[0]           ---           deg adv @ crank
876     3090    sp_tble[14][ 1] float       spk adv for maps[14], rpms[1]           ---           deg adv @ crank
877     3094    sp_tble[14][ 2] float       spk adv for maps[14], rpms[2]           ---           deg adv @ crank
878     3098    sp_tble[14][ 3] float       spk adv for maps[14], rpms[3]           ---           deg adv @ crank
879     3102    sp_tble[14][ 4] float       spk adv for maps[14], rpms[4]           ---           deg adv @ crank
880     3106    sp_tble[14][ 5] float       spk adv for maps[14], rpms[5]           ---           deg adv @ crank
881     3110    sp_tble[14][ 6] float       spk adv for maps[14], rpms[6]           ---           deg adv @ crank
882     3114    sp_tble[14][ 7] float       spk adv for maps[14], rpms[7]           ---           deg adv @ crank
883     3118    sp_tble[14][ 8] float       spk adv for maps[14], rpms[8]           ---           deg adv @ crank
884     3122    sp_tble[14][ 9] float       spk adv for maps[14], rpms[9]           ---           deg adv @ crank
885     3126    sp_tble[14][10] float       spk adv for maps[14], rpms[10]          ---           deg adv @ crank
886     3130    sp_tble[14][11] float       spk adv for maps[14], rpms[11]          ---           deg adv @ crank
887     3134    sp_tble[14][12] float       spk adv for maps[14], rpms[12]          ---           deg adv @ crank
888     3138    sp_tble[14][13] float       spk adv for maps[14], rpms[13]          ---           deg adv @ crank
889     3142    sp_tble[14][14] float       spk adv for maps[14], rpms[14]          ---           deg adv @ crank
890     3146    sp_tble[14][15] float       spk adv for maps[14], rpms[15]          ---           deg adv @ crank

891     3150    sp_tble[15][ 0] float       spk adv for maps[15], rpms[0]           ---           deg adv @ crank
892     3154    sp_tble[15][ 1] float       spk adv for maps[15], rpms[1]           ---           deg adv @ crank
893     3158    sp_tble[15][ 2] float       spk adv for maps[15], rpms[2]           ---           deg adv @ crank
894     3162    sp_tble[15][ 3] float       spk adv for maps[15], rpms[3]           ---           deg adv @ crank
895     3166    sp_tble[15][ 4] float       spk adv for maps[15], rpms[4]           ---           deg adv @ crank
896     3170    sp_tble[15][ 5] float       spk adv for maps[15], rpms[5]           ---           deg adv @ crank
897     3174    sp_tble[15][ 6] float       spk adv for maps[15], rpms[6]           ---           deg adv @ crank
898     3178    sp_tble[15][ 7] float       spk adv for maps[15], rpms[7]           ---           deg adv @ crank
899     3182    sp_tble[15][ 8] float       spk adv for maps[15], rpms[8]           ---           deg adv @ crank
900     3186    sp_tble[15][ 9] float       spk adv for maps[15], rpms[9]           ---           deg adv @ crank
901     3190    sp_tble[15][10] float       spk adv for maps[15], rpms[10]          ---           deg adv @ crank
902     3194    sp_tble[15][11] float       spk adv for maps[15], rpms[11]          ---           deg adv @ crank
903     3198    sp_tble[15][12] float       spk adv for maps[15], rpms[12]          ---           deg adv @ crank
904     3202    sp_tble[15][13] float       spk adv for maps[15], rpms[13]          ---           deg adv @ crank
905     3206    sp_tble[15][14] float       spk adv for maps[15], rpms[14]          ---           deg adv @ crank
906     3210    sp_tble[15][15] float       spk adv for maps[15], rpms[15]          ---           deg adv @ crank

907     3214    inj_flow_ramp   float       average injector flow rate on           .050417e-7    lbs/ microsec
                                            open ramp (from bkpt to fully           (18.2#/ hr)
                                            open) @ operating pressure
908     3218    inj_flow_max    float       injector flow rate @ operating          .152778e-7    lbs/ microsec
                                            fuel pressure w inj fully open          (55 # / hr)
909     3222    inj_flow_close  float       average injector flow rate on           .102361e-7    lbs/ microsec
                                            closing ramp @ op. pressure             (36.9#/ hr)

910     3226    spk_adv_max     float       max allowable spark advance             70            crank deg BTDC

911     3230    no_vmaps        shrt int    no of map points in veaf_maps           7             ---
                                            array below; these are manifold
                                            air pressures for veaf_table
912     3232    no_vrpms        shrt int    no of rpms in veaf_rpms                 14            ---
                                            array below; these are rpms
                                            for veaf_table
913     3234    veaf_maps[0]    shrt int    manifold air pressure for               0             KPa x 10
                                            veaf_table[0][.]
914     3236    veaf_maps[1]    shrt int    map for veaf_table[1][.]                323           KPa x 10
915     3238    veaf_maps[2]    shrt int    map for veaf_table[2][.]                492           KPa x 10
916     3240    veaf_maps[3]    shrt int    map for veaf_table[3][.]                661           KPa x 10
917     3242    veaf_maps[4]    shrt int    map for veaf_table[4][.]                831           KPa x 10
918     3244    veaf_maps[5]    shrt int    map for veaf_table[5][.]                983           KPa x 10
919     3246    veaf_maps[6]    shrt int    map for veaf_table[6][.]                1100          KPa x 10
920     3248    veaf_maps[7]    shrt int    map for veaf_table[7][.]                ---           KPa x 10
921     3250    veaf_maps[8]    shrt int    map for veaf_table[8][.]                ---           KPa x 10
922     3252    veaf_maps[9]    shrt int    map for veaf_table[9][.]                ---           KPa x 10
923     3254    veaf_maps[10]   shrt int    map for veaf_table[10][.]               ---           KPa x 10
924     3256    veaf_maps[11]   shrt int    map for veaf_table[11][.]               ---           KPa x 10
925     3258    veaf_maps[12]   shrt int    map for veaf_table[12][.]               ---           KPa x 10
926     3260    veaf_maps[13]   shrt int    map for veaf_table[13][.]               ---           KPa x 10
927     3262    veaf_maps[14]   shrt int    map for veaf_table[14][.]               ---           KPa x 10
928     3264    veaf_maps[15]   shrt int    map for veaf_table[15][.]               ---           KPa x 10
929     3266    veaf_maps[16]   shrt int    map for veaf_table[16][.]               ---           KPa x 10
930     3268    veaf_maps[17]   shrt int    map for veaf_table[17][.]               ---           KPa x 10
931     3270    veaf_maps[18]   shrt int    map for veaf_table[18][.]               ---           KPa x 10
932     3272    veaf_maps[19]   shrt int    map for veaf_table[19][.]               ---           KPa x 10

933     3274    veaf_rpms[0]    shrt int    rpm for veaf_table[.][0]                500           rpm
934     3276    veaf_rpms[1]    shrt int    rpm for veaf_table[.][1]                1000          rpm
935     3278    veaf_rpms[2]    shrt int    rpm for veaf_table[.][2]                1750          rpm
936     3280    veaf_rpms[3]    shrt int    rpm for veaf_table[.][3]                2500          rpm
937     3282    veaf_rpms[4]    shrt int    rpm for veaf_table[.][4]                3000          rpm
938     3284    veaf_rpms[5]    shrt int    rpm for veaf_table[.][5]                3500          rpm
939     3286    veaf_rpms[6]    shrt int    rpm for veaf_table[.][6]                4000          rpm
940     3288    veaf_rpms[7]    shrt int    rpm for veaf_table[.][7]                4500          rpm
941     3290    veaf_rpms[8]    shrt int    rpm for veaf_table[.][8]                5000          rpm
942     3292    veaf_rpms[9]    shrt int    rpm for veaf_table[.][9]                5250          rpm
943     3294    veaf_rpms[10]   shrt int    rpm for veaf_table[.][10]               5500          rpm
944     3296    veaf_rpms[11]   shrt int    rpm for veaf_table[.][11]               6000          rpm
945     3298    veaf_rpms[12]   shrt int    rpm for veaf_table[.][12]               7000          rpm
946     3300    veaf_rpms[13]   shrt int    rpm for veaf_table[.][13]               7500          rpm
947     3302    veaf_rpms[14]   shrt int    rpm for veaf_table[.][14]               ---           rpm
948     3304    veaf_rpms[15]   shrt int    rpm for veaf_table[.][15]               ---           rpm
949     3306    veaf_rpms[16]   shrt int    rpm for veaf_table[.][16]               ---           rpm
950     3308    veaf_rpms[17]   shrt int    rpm for veaf_table[.][17]               ---           rpm
951     3310    veaf_rpms[18]   shrt int    rpm for veaf_table[.][18]               ---           rpm
952     3312    veaf_rpms[19]   shrt int    rpm for veaf_table[.][19]               ---           rpm

953     3314    no_smaps        shrt int    no of map points in spark_maps          9             ---
                                            array below; these are manifold
                                            air pressures for spark_table
954     3316    no_srpms        shrt int    no of rpms in spark_rpms                14            ---
                                            array below; these are rpms
                                            for spark_table
955     3318    spark_maps[0]   shrt int    manifold air pressure for               0             KPa x 10
                                            spark_table[0][.]
956     3320    spark_maps[1]   shrt int    map for spark_table[1][.]               300           KPa x 10
957     3322    spark_maps[2]   shrt int    map for spark_table[2][.]               400           KPa x 10
958     3324    spark_maps[3]   shrt int    map for spark_table[3][.]               500           KPa x 10
959     3326    spark_maps[4]   shrt int    map for spark_table[4][.]               600           KPa x 10
960     3328    spark_maps[5]   shrt int    map for spark_table[5][.]               700           KPa x 10
961     3330    spark_maps[6]   shrt int    map for spark_table[6][.]               800           KPa x 10
962     3332    spark_maps[7]   shrt int    map for spark_table[7][.]               900           KPa x 10
963     3334    spark_maps[8]   shrt int    map for spark_table[8][.]               1100          KPa x 10
964     3336    spark_maps[9]   shrt int    map for spark_table[9][.]               ---           KPa x 10
965     3338    spark_maps[10]  shrt int    map for spark_table[10][.]              ---           KPa x 10
966     3340    spark_maps[11]  shrt int    map for spark_table[11][.]              ---           KPa x 10
967     3342    spark_maps[12]  shrt int    map for spark_table[12][.]              ---           KPa x 10
968     3344    spark_maps[13]  shrt int    map for spark_table[13][.]              ---           KPa x 10
969     3346    spark_maps[14]  shrt int    map for spark_table[14][.]              ---           KPa x 10
970     3348    spark_maps[15]  shrt int    map for spark_table[15][.]              ---           KPa x 10

971     3350    spark_rpms[0]   shrt int    rpm for spark_table[.][0]               0             rpm
972     3352    spark_rpms[1]   shrt int    rpm for spark_table[.][1]               200           rpm
973     3354    spark_rpms[2]   shrt int    rpm for spark_table[.][2]               400           rpm
974     3356    spark_rpms[3]   shrt int    rpm for spark_table[.][3]               600           rpm
975     3358    spark_rpms[4]   shrt int    rpm for spark_table[.][4]               800           rpm
976     3360    spark_rpms[5]   shrt int    rpm for spark_table[.][5]               1000          rpm
977     3362    spark_rpms[6]   shrt int    rpm for spark_table[.][6]               1200          rpm
978     3364    spark_rpms[7]   shrt int    rpm for spark_table[.][7]               1400          rpm
979     3366    spark_rpms[8]   shrt int    rpm for spark_table[.][8]               1600          rpm
980     3368    spark_rpms[9]   shrt int    rpm for spark_table[.][9]               1800          rpm
981     3370    spark_rpms[10]  shrt int    rpm for spark_table[.][10]              2000          rpm
982     3372    spark_rpms[11]  shrt int    rpm for spark_table[.][11]              2500          rpm
983     3374    spark_rpms[12]  shrt int    rpm for spark_table[.][12]              3000          rpm
984     3376    spark_rpms[13]  shrt int    rpm for spark_table[.][13]              8000          rpm
985     3378    spark_rpms[14]  shrt int    rpm for spark_table[.][14]              ---           rpm
986     3380    spark_rpms[15]  shrt int    rpm for spark_table[.][15]              ---           rpm

987     3382    pw_min          shrt int    minimum possible fuel                   500           microsec
                                            pulsewidth                              (.5 ms)
988     3384    max_duty_cycle  shrt int    maximum percentage of the 0             80            %(whole no.)
                                            to 720 deg engine cycle allowed
                                            for fuel pulsewidth; max pw (time)
                                            is calculated from this as function
                                            of rpm
989     3386    cyl_fuel[0]     shrt int    fractional change in fuel pulse-        100           %(whole no.)
                                            width for individual cylinder                         E.g., 105 would
                                            tuning; it is always applied,                         be 5% incr in
                                            but only to the basic pw calcu-                       pw; 95 would
                                            lated from veaf_table, not to                         be 5% decr
                                            any enrichment or +/- button.
                                            Can be set to 0 to temporarily
                                            kill a cylinder. This is for the
                                            1st cylinder in the firing order.
990     3388    cyl_fuel[1]     shrt int    pw tuning for 2nd cyl in f.o.           100           %(whole no.)
991     3390    cyl_fuel[2]     shrt int    pw tuning for 3rd cyl in f.o.           100           %(whole no.)
992     3392    cyl_fuel[3]     shrt int    pw tuning for 4th cyl in f.o.           100           %(whole no.)
993     3394    cyl_fuel[4]     shrt int    pw tuning for 5th cyl in f.o.           100           %(whole no.)
994     3396    cyl_fuel[5]     shrt int    pw tuning for 6th cyl in f.o.           100           %(whole no.)
995     3398    cyl_fuel[6]     shrt int    pw tuning for 7th cyl in f.o.           100           %(whole no.)
996     3400    cyl_fuel[7]     shrt int    pw tuning for 8th cyl in f.o.           100           %(whole no.)

997     3402    cyl_spark[0]    shrt int    fractional change in spark              100           %(whole no.)
                                            advance for individual cylinder                       E.g., 105 would
                                            tuning; it is always applied,                         be 5% incr in
                                            but only to the basic spk calcu-                      adv; 95 would
                                            lated from spark_table, not to                        be 5% decr
                                            any warmup spk or +/- button.
                                            This is for the 1st cylinder in
                                            the firing order.
998     3404    cyl_spark[1]    shrt int    spk tuning for 2nd cyl in f.o.          100           %(whole no.)
999     3406    cyl_spark[2]    shrt int    spk tuning for 3rd cyl in f.o.          100           %(whole no.)
1000    3408    cyl_spark[3]    shrt int    spk tuning for 4th cyl in f.o.          100           %(whole no.)
1001    3410    cyl_spark[4]    shrt int    spk tuning for 5th cyl in f.o.          100           %(whole no.)
1002    3412    cyl_spark[5]    shrt int    spk tuning for 6th cyl in f.o.          100           %(whole no.)
1003    3414    cyl_spark[6]    shrt int    spk tuning for 7th cyl in f.o.          100           %(whole no.)
1004    3416    cyl_spark[7]    shrt int    spk tuning for 8th cyl in f.o.          100           %(whole no.)

1005    3418    stop_inj        shrt int    point before intake close at            570           crank deg
                                            which will stop fuel injection;                       (0 - 720)
                                            = intake close - f * intake duration,
                                            where f is some fraction between
                                            0 and 1. E.g., = 616 - .15 * 306
                                            = 570.
1006    3420    exh_close       shrt int    point at which exhaust valvea           402           crank deg
                                            closes                                                (0 - 720)
1007    3422    deg_reach_      shrt int    No. of crank deg for air to travel      73            crank deg
                valve_air                   thru cylinder port to int. valve.                     (increment)
1008    3424    inj_adv         shrt int    number of degrees change in the         0             crank deg
                                            point at which the program calcu-                     (increment,
                                            lates fuel injection should start;                    + is toward
                                            used for tuning                                       BTDC,ie, adv)
1009    3426    fuel_spd_cof    float       Coefficient used to calculate no.       .0296469      ---
                                            of crank deg for fuel to travel
                                            thru cylinder port to int. valve.

1010    3430    t_fpump_shut    int         amount of time allowed with no          200000         ms x 10
                                            crank rotation before the fuel          (20 sec)
                                            pump is shut off

1011    3434    rpm_clr_choke   shrt int    maximum rpm for cutting off fuel        300           rpm
                                            during cranking; represents fastest
                                            rpm with starter motor only.
1012    3436    tps_clr_choke   shrt int    minimum throttle opening for cut-       900           % x 10
                                            ting off fuel during cranking.

1013    3438    start_inj_batch shrt int    no. of rel deg at which to fire         120           crank deg
                                            injectors in batch mode; each in-
                                            jector will fire @ d and d+360 deg.